## Slide 1: Mips CPU逻辑设计 ——数据通路设计
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (1)
Single Circle 硬件实现
Pipeline Circle 硬件实现
本章的目标：

## Slide 2: Single Circle Outline
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (2)
每指令单周期实现
=> Data path 上的资源每指令周期最多用一次
=>如果需要多次使用就需要硬件上有多个: memory, ALU/adders, …
单周期Datapath设计
  5 通用步骤

## Slide 3
CPU的构成
(Control Unit)
ALU
CPU
(Datapath)
...
I/O接口
寄存器堆
多路选择器
计算机
存储器
控制部件
数据路径

## Slide 4: 处理器设计: step-by-step
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (3)
分析指令集 => datapath 需求
  每个指令的含义都用寄存器传输级（RTL）给出
  datapath 必须包含ISA所需要的各个寄存器
    为了实现功能还需要一些额外的寄存器
  datapath 必须支持每一类寄存器转移操作
选择datapath中包含的模块,确定这些模块的功能,时序
组装datapath
根据指令集决定datapath中需要的控制信号
设计控制信号逻辑

## Slide 5: The MIPS Instruction Formats
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (4)
R-type
I-type
J-type
op
target address
0
31
6 bits 26 bits
各个域分别是:
  op: 指令操作
  rs, rt, rd: 源,目的寄存器序号
  shamt: 移位量
  funct: 对op类操作，确定详细的操作类型
  address / immediate: 立即数或者地址
  target address: 目标地址
op | rs | rt | rd | shamt | funct
0
三类MIPS指令:
31 26 21 16 11 6
immediate
0
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
26 21 16
31
16 bits
op rs rt
6 bits 5 bits 5 bits
26

## Slide 6: Step 1b: 从指令分析datapath组成
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (6)
存储器
  一个指令存储器、一个数据存储器
寄存器(32 x 32bit)
  可以为 RS提供读取
  可以为 RT提供读取
  可以为RT或者RD提供写入端口
PC(程序记数)
扩展电路: 为立即数提供
加法/减法等运算：两个寄存器之间的或者是一个寄存器一个经过扩展后的立即数之间
PC更新电路：可以加4或者加上一个立即数扩展

## Slide 7: Step 2: datapath组成
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (7)
组合逻辑电路部分
存储单元(“状态”)

## Slide 8: 数据通路部件
加法器(Adder)
多路选择器 (MUX)
算术逻辑部件(ALU)
32
A
B
32
Y
32
Select
MUX
32
32
A
B
32
Result
Zero
OP
ALU
32
32
A
B
32
Sum
Carry
Adder
CarryIn
3
Decoder
out0
out1
out7
out2
译码器(Decoder)
何时要用到adder, ALU, MUX or Decoder?
控制信号
组合逻辑元件的特点
其输出只取决于当前的输入
定时：所有输入到达后，经过一定的逻辑门延时，输出端改变，并保持到下次改变，不需要时钟信号来定时
二选一
或多选一
加法器需要什么控制信号?
Notes: Based on the Register Transfer Language examples we have so far, we know we will need the following combinational logic elements.
We will need an adder to update the program counter.
A MUX to select the results.
And finally, an ALU to do various arithmetic and logic operation.

## Slide 9: 状态元件：时序逻辑电路
状态(存储)元件的特点
  具有存储功能，在时钟控制下输入状态被写到电路中，直到下一个时钟到达
  输入端状态由时钟决定何时写入，输出端状态随时可读出
定时方式:规定信号何时写入状态元件或何时从状态元件读出
  边沿触发(edge-triggered)方式
    状态单元中的值只在时钟边沿改变。每个时钟周期改变一次
最简单的状态单元
  D触发器：一个时钟输入、一个状态输入、一个状态输出
cycle time
rising edge
falling edge
上升沿(rising edge) 触发：在时钟正跳变时进行读/写
下降沿(falling edge)触发：在时钟负跳变时进行读/写

## Slide 10: 回顾——D触发器
切记：状态单元的输入信息总是在一个时钟边沿到达后的“Clk-to-Q”时才被写入到单元中，此时的输出才反映新的状态值
数据通路中的状态元件有两种：寄存器(组) + 存储器
Q总是在clk-Q后跟着D变化
这段时间D变化不影响Q
建立时间(Set Time):在触发时钟边沿之前输入必须稳定
保持时间(Hold Time):在触发时钟边沿之后输入必须保持
Clock-to-Q-time:在触发时钟边沿，输出并不能立即变化

## Slide 11: 存储单元: 寄存器(Basic Building Block)
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (9)
寄存器
  类似D触发器，有以下不同
    N-bit 输入输出
    可以同时从两个口读取,
    有写入使能端
  写入使能:
    禁止时(0): 寄存器内容不变
    使能时(1): 改变
Clk
Write Enable
Data In N
Data Out N
寄存器0
寄存器1
…
寄存器31
多路复用
多路复用
读数据2
读数据1
读寄存器号1

## Slide 12: 存储单元: 寄存器组
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (10)
寄存器组包含 32 registers:
两个 32-bit 输出总线: busA and busB
一个32-bit 输入总线: busW
寄存器组中的寄存器选择:
RA (number) 选出哪个32位寄存器的数据放在busA (data)
RB (number)选出哪个32位寄存器的数据放在busB (data)
RW (number)选出哪个32位寄存器的数据将通过busW被写入
(当WE=1时)
时钟 (CLK)
  CLK 只在写人时发挥作用
  读取电路总能读到值
    RA or RB valid => busA or busB valid after “access time.”
busW
Clk
32
busA
32
busB
32
5 5
Write Enable 5
RW RA RB
32 32-bit Registers

## Slide 13: Mips寄存器结构
32个通用寄存器
程序计数器PC
HI LO

## Slide 14: 存储单元: 存储器
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (11)
存储器(容量大)
  一个输入总线: 数据输入
  一个输出总线: 数据输出
存储器选择:
通过地址线Address 选择哪个32位字被放在数据输出总线上
Write Enable = 1: 通过address选择哪个地址的32位字写为输入总线的数据
Clock input (CLK)
  CLK input 只在写入有效
  在读出时, 类似于组合逻辑:
    Address valid => Data Out valid after “access time.”
Write E
Data In 32
Clk
DataOut
32
nable |  | Add
ress

## Slide 15
单周期CPU
单周期(Single-Cycle) CPU执行一条指令用一个时钟周期
(最简单的执行方式
)
Clock
时钟上升沿(0到 1的变化）
下降沿
一个周期
指令1
在时钟上升沿保存指令的结果和下一条指令的地址
指令2
指令3
指令4

## Slide 16: 单周期数据通路设计
问题: 将 “执行整个指令”的块做为一个整体
  太大(该块要执行从取指令开始的所有操作)
  效率不高
解决方案: 将 “执行整个指令” 的操作分解为多个阶段 (stage)，然后将所有阶段连接在一起产生整个datapath
  每一阶段更小，从而更容易设计
  方便优化其中一个阶段，而不必涉及其他阶段

## Slide 17: Generic Steps of Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Reg.
Write
单周期数据通路设计

## Slide 18: 取指令单元IF
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (15)
所有指令都公用的单元
  Fetch the Instruction: mem[PC]
  更新PC:
顺序指令时: PC <= PC + 4
分支跳转时:
PC <= “something else”
Instruction Word
32
Address
Instruction Memory
PC
Clk
Next Address Logic
Stages of the Datapath (1/5)
顺序：先取指令，再改变PC的值(具体实现可以并行)
决不能先改变PC的值，再取指令

## Slide 19: Stages of the Datapath (2/5)
Stage 2: 指令译码Instruction Decode
  在取到指令后, 下一步从各域(fields)中得到数据(对必要的指令数据进行解码)
  首先，读出Opcode，以决定指令类型及字段长度
  接下来，从相关部分读出数据
    for add, read two registers
    for addi, read one register
    for jal, no reads necessary

## Slide 20: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
  and
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction
Fetch
PC = PC+4
Decode
Exec

## Slide 21: Reading Registers “Just in Case”
Note that both RegFile read ports are active for all instructions during the Decode cycle using the rs and rt instruction field addresses
  Since haven’t decoded the instruction yet, don’t know what the instruction is !
  Just in case the instruction uses values from the RegFile do “work ahead” by reading the two source operands
Which instructions do make use of the RegFile values?
Also, all instructions (except j) use the ALU after reading the registers
Why? memory-reference? arithmetic? control flow?
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 22: Stages of the Datapath (3/5)
Stage 3: ALU (Arithmetic-Logic Unit)
  大多数指令的实际工作在此部完成: 算术指令 (+, -, *, /), shifting, logic (&, |), comparisons (slt)
  what about loads and stores?
    lw $t0, 40($t1)
    要访问的内存地址 = $t1的值 + 40
    so we do this addition in this stage

## Slide 23: Stages of the Datapath (4/5)
Stage 4: 内存访问Memory Access
  事实上只有load和store指令在此stage会做事; 其它指令在此阶段空闲idle或者直接跳过本阶段
  由于load和store需要此步，因此需要一个专门的阶段 stage来处理他们
  由于cache系统的作用，该阶段有望加速
  如果没有caches，本阶段stage会很慢

## Slide 24: Stages of the Datapath (5/5)
Stage 5: 写寄存器Register Write
  大多数指令会将计算结果写到寄存器
  例如: arithmetic, logical, shifts, loads, slt
  what about stores, branches, jumps?
    don’t write anything into a register at the end
    these remain idle during this fifth stage or skip it all together

## Slide 25: 数据路径—R型指令
Op
rs
rt
rd
shamt
func
Ra
Clock
Rb
Rw
Data
32 32-bit
Registers
ALU
Zero
译码
Operation
Wn
R format operations (add, sub, slt, and, or)
指令的意义:寄存器rs中的数据和寄存器rt中的数据相加，结果存放在寄存器rd中。把PC + 4写入PC

## Slide 26: 定时:完整周期
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (17)
32
Result
ALUctr
Clk
busW
32
busA
32
busB
32
RegWr 5
5 5
Rw Ra Rb
32 32-bit
Registers
Rd Rs Rt
ALU
Clk
PC
Rs, Rt, Rd, Op, Func
Clk-to-Q
ALUctr
指令存储器访问延迟
Old Value
New Value
控制逻辑电路的延迟
busA, B
Register File 访问时间(延迟)
Old Value
New Value
busW
ALU 延迟
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write Occurs Here
RegWr
Old Value
New Value

## Slide 27: 3-Operand ALU Data Path 需要的控制信号
Register File
RA2
RD2
RA1 WA
RD1
WD WE
Rd: <15:11>
PC
+4
A
Instruction Memory
D
Rt: <20:16>
ALU
A
B
ALUFN
Control Logic
WERF
ALUFN
WERF
00
32
32
32
Rs: <25:21>
000000
rs rt rd
100XXX
00000
R-type:
ALU with Reguster operands Reg[rd]  Reg[rs] op Reg[rt]
WERF!
OP
ALU
All of these instructions modify the contents of their destination
register, r , thus, the
d
Write-Enable-Register-File
control line, WERF
is always a “1”

## Slide 28: Shift Instructions
Register
File
RA1
RA2
RD1
RD2
WA
WD
WE
Rd: <15:11>
PC
+4
Instruction
Memory
A
D
Rt: <20:16>
ALU
A
B
ALUFN
Control Logic
WERF
ALUFN
WERF
00
32
000000
rs
rt
rd
000XXX
shamt
R-type: ALU with Register operands sll: Reg[rd]  Reg[rt] (shift) shamt
sllv: Reg[rd]  Reg[rt] (shift) Reg[rs]
ASEL
Rs: <25:21>
ASEL
1
0
shamt:<10:6>
ASEL!
指令的意义:寄存器rt中的数据左移sa位，结果存放在寄存器rd中。把PC + 4写入PC
与sll类似的指令
: srl, sra

## Slide 29: LW操作
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (19)
R[rt] <= Mem[R[rs] + SignExt[imm16]]
Example: lw rt, imm16(rs)
op | rs | rt | immediate
0
31 26 21 16
16 bits
ALUctr
busW
32
Clk
busA
32
busB
32
RegWr 5
Rw Ra Rb
32 32-bit Registers
6 bits 5 bits 5 bits Rd Rt
RegDst
Extender
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Clk
WrEn Adr
Data Memory
32
ALU
32
MemWr
Mux
W_Src
?? Data In
32
Rs Rt?
5 5

## Slide 30: Load Instruction 需要的控制信号
WA
PC
+4
Instruction
Memory
A
D
Register
File
RA1
RA2
RD1
RD2
ALU
A
B
WA
WD
WE
ALUFN
Control Logic
Imm: <15:0>
Data Memory
RD
WD
R/W
Adr
Wr
WDSEL
0 1 2
BSEL
WDSEL
ALUFN
Wr
WERF
WERF
00
32
32
Rd:<15:11>
Rt:<20:16>
0
1
BSEL
SEXT
100011
rs
rt
immediate
I-type: Load
Reg[rt]  Mem[Reg[rs] + SEXT(immediate)]
ASEL
Rt: <20:16>
Rs: <25:21>
SEXT
BSEL
0
1
SEXT
ASEL
1
0
shamt:<10:6>
BSEL=1加数选择立即数
和选寄存器写入rt
SEXT=1立即数符号扩展
WDSEL=1选择存储器内容写入寄存器
ALUFN=add
Wr=0
WERF=1寄存器写使能
ASEL=0选rs作为被加数

## Slide 31: SW操作
Mem[ R[rs] + SignExt[imm16] ] <= R[rt]
Example: sw rt, imm16(rs)
op | rs | rt | immediate
0
31 26 21 16
32
ALUctr
busW
32
Clk
busA
32
32
busB
RegWr 5
Rw Ra Rb
32 32-bit Registers
Rs Rt
5 5
6 bits 5 bits 5 bits Rd Rt
RegDst
Extende
r
Mux
Mux
32
16
imm16
ExtOp ALUSrc
Data In
32 Clk | WrEn Adr Data Memory
16 bits
MemWr
ALU
32
Mux
W_Src

## Slide 32: Store Instruction 需要的控制信号
WA
PC
+4
Instruction
Memory
A
D
Register
File
RA1
RA2
RD1
RD2
ALU
A
B
WA
WD
WE
ALUFN
Control Logic
Imm: <15:0>
Data Memory
RD
WD
R/W
Adr
Wr
WDSEL
0 1 2
BSEL
WDSEL
ALUFN
Wr
WERF
WERF
00
32
Rd:<15:11>
Rt:<20:16>
0
1
SEXT
ASEL
10X011
rs
rt
immediate
I-type: Store
Mem[Reg[rs] + SEXT(immediate)]  Reg[rt]
Rt: <20:16>
BSEL
No WERF!
Rs: <25:21>
ASEL
1
0
SEXT
BSEL
0
1
SEXT
shamt:<10:6>
BSEL=1加数选择立即数
和选寄存器写入rt
SEXT=1立即数符号扩展
WDSEL=1选择存储器内容写入寄存器
ALUFN=add
Wr=1
WERF=1寄存器写使能
ASEL=0选rs作为被加数

## Slide 33: JMP Instructions
WA
PC
+4
A
Instruction Memory
D
Register File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
Control Logic
RD
WD R/W
Data Memory
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
32
PC+4
Rt: <20:16>
00001X
26-bit constant
J-type:
j: PC  (PC & 0xf0000000) | 4*(immediate) jal: PC  (PC & 0xf0000000) | 4*(immediate);
Reg[31]  PC + 4
PC<31:29>:J<25:0>:00
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
Rs: <25:21>
BSEL
0
ASEL 1
SEXT
shamt:<1
0 1
 | SEXT | 
0:6> |  | 
PCSEL
6 5 4 3 2 1 0
WASEL
Rd:<15:11> 0
WA
Rt:<20:16> 1
“31” 2
“27” 3
Imm: <15:0>
The first step is to provide some means for loading the PC with a value other than PC+4.
A mux with a PCSEL
control line provides this.
To support the JAL instruction we need to save PC+4 into
register “31”. This requires that we rework the mux on the WA input of the register file to allow the constant “31” to be selected and that we provide a path so that
PC+4 can be written into the register file as controlled by
WDSEL.
Jal指令，WDSEL=0选择PC+4写入$31
寄存器写入输入选择WASEL选$31
PCSEL=2选26位立即数扩展后的结果作为PC值
WDSEL=0选择PC+4写入$31

## Slide 34: The Branch Instruction
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (21)
从存储器取指令计算分支条件
计算下一个指令的地址
PC <= PC + 4 + { SignExt(imm16) , 2b00 }
else
  PC <= PC + 4
op | rs | rt | immediate
0
16
21
26
31
16 bits
6 bits 5 bits 5 bits
Beq rs, rt, imm16
  mem[PC]
  Equal <= (R[rs] == R[rt])
  if (Equal)

## Slide 35: 分支指令的datapath
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (22)
beq rs, rt, imm16
Datapath generates condition (equal)
op | rs | rt | immediate
0
31 26 21 16
16 bits
6 bits 5 bits
32
imm16
PC
Clk
00
Adder
Mux
Adder
4
PCSrc
Clk
busW
32
busA
busB
32
RegWr 5
Rw Ra Rb
32 32-bit Registers
Rs Rt
5 5
Equal?
Cond
PC Ext
5 bits
Inst Address

## Slide 36: BEQ/BNE Instructions 需要的控制信号
WA
PC
+4
Instruction
Memory
A
D
Register
File
RA1
RA2
RD1
RD2
ALU
A
B
WA
WD
WE
ALUFN
Control Logic
Data Memory
RD
WD
R/W
Adr
Wr
WDSEL
0 1 2
BSEL
WDSEL
ALUFN
Wr
J:<25:0>
PCSEL
WERF
WERF
00
32
PC+4
Rt: <20:16>
Imm: <15:0>
ASEL
SEXT
10X011
immediate
rs
rt
R-type: Branch Instructions
if (Reg[rs] == Reg[rt]) PC  PC + 4 + 4*SEXT(immediate)
if (Reg[rs] != Reg[rt]) PC  PC + 4 + 4*SEXT(immediate)
+
x4
BT
Z
Z
BT
PC<31:29>:J<25:0>:00
Why add, another adder? Couldn’t we reuse the one in the ALU? Nope, it needs to do a subtraction.
That “x4” unit is trivial. I’ll just wire the input shifted over 2–bit positions.
WASEL
Rs: <25:21>
ASEL
1
0
SEXT
BSEL
0
1
SEXT
shamt:<10:6>
PCSEL
0
1
2
3
4
5
6
WASEL
Rd:<15:11>
Rt:<20:16>
31
0
1
2

## Slide 37: Jump Indirect Instructions
WA
PC
+4
A
Instruction Memory
D
Register File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
Control Logic
RD
WD R/W
Data Memory
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
32
PC+4
Rt: <20:16>
R-type:
Jump Indirect, Jump and Link Indirect
jr: jalr:
PC  Reg[rs]
PC  Reg[rs], Reg[rd]  PC + 4
x4
+
BT
Z
Z
BT
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
PC<31:29>:J<25:0>:00
000000
rs rt rd
00100X
00000
JT
JT
Rs: <25:21>
0 1
SEXT
BSEL
0
ASEL 1
SEXT
shamt:<10:6>
PCSEL
6 5 4 3 2 1 0
WASEL
Rd:<15:11> 0
WA
Rt:<20:16> 1
“31” 2
“27” 3
Imm: <15:0>
The instructions, JR and JALR, set the next PC using the
contents of the register specified by rs. This requires the the output of the first register port be routed to the mux used to load the next PC.
The JALR
instruction reuses the connections from JAL that allow PC+4 to be stored in “31”.

## Slide 38: Loose Ends
WA
PC
+4
A
Instruction Memory
D
Register File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
Control Logic
RD
WD R/W
Data Memory
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
32
PC+4
Rt: <20:16>
I-type: set on less than & set on less than unsigned immediate
slti: if (Reg[rs] < SEXT(imm)) Reg[rt]  1; else Reg[rt]  0
sltiu: if (Reg[rs] < SEXT(imm)) Reg[rt]  1; else Reg[rt]  0
x4
+
BT
BT
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
PC<31:29>:J<25:0>:00
JT
JT
001XXX
immediate
rs rt
Reminder:
To evaluate
(A < B) we
first compute
A-B and look at the flags.
LT = N  V LTU = C
NV C Z
Z N V C
Rs: <25:21>
0 1
SEXT
BSEL
0
ASEL 1
SEXT
shamt:<10:6>
PCSEL
6 5 4 3 2 1 0
WASEL
Rd:<15:11> 0
WA
Rt:<20:16> 1
“31” 2
“27” 3
Imm: <15:0>
The SET immediate instructions use the ALU paths that we added to
route a “0” or a “1” to the ALU output based on the condition flags that result from subtracting a sign-extended immediate value from rs (BSEL=1).
WDSEL = 1
and WERF = 1
有立即数的操作
rd?
R[rt] <= R[rs] op ZeroExt[imm16]

## Slide 39: More Loose Ends
WA
PC
+4
A
Instruction Memory
D
Register File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
Control Logic
RD
WD R/W
Data Memory
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
PC+4
32
Rt: <20:16>
R-type: set on less than & set on less than unsigned
slt: if (Reg[rs] < Reg[rt]) Reg[rd]  1; else Reg[rd]  0
sltu: if (Reg[rs] < Reg[rt]) Reg[rd]  1; else Reg[rd]  0
x4
+
BT
BT
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
PC<31:29>:J<25:0>:00
JT
JT
000000
rs rt rd
10101X
00000
Z N V C
NV C Z
Rs: <25:21>
0 1
SEXT
BSEL
0
ASEL 1
SEXT
shamt:<10:6>
PCSEL
6 5 4 3 2 1 0
WASEL
Rd:<15:11> 0
WA
Rt:<20:16> 1
“31” 2
“27” 3
Imm: <15:0>
Similarly, the SET ALU
route a “0” or a “1” to the ALU output based on the condition flags that result from subtracting a rt from rs (BSEL=0).
Reminder:
To evaluate
(A < B) we
first compute
A-B and look at the flags.
LT = N  V LTU = C
WDSEL = 1
and WERF = 1

## Slide 40: LUI Ends
WA
PC
+4
A
Instruction Memory
D
Register File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
Control Logic
RD
WD R/W
Data Memory
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
32
PC+4
Rt: <20:16>
Imm: <15:0>
I-type: Load upper immediate
lui:
Reg[rt]  Immediate << 16
x4
+
BT
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
PC<31:29>:J<25:0>:00
BT
JT
JT
Z N V C
NV C Z
immediate
001XXX 00000
r
t
Rs: <25:21>
SEXT
BSEL
0
1
SEXT
PCSEL
6 5 4 3 2 1 0
WASEL
Rd:<15:11> 0
WA
Rt:<20:16> 1
“31” 2
“27” 3
ASEL
shamt:<10:6>
“16”
0 1 2
We are using the ALU’s barrel shifter to implement LUI. This requires
another input to the mux on the A input of the ALU, and we need to configure the ALU to shift left, ASEL = 2, WDSEL=1 WASEL=1, and WERF=1.

## Slide 41: Reset, Interrupts, and Exceptions
FIRST, we need some way to get our machine into a known initial state. This doesn’t mean that all registers will be initialized, just that we’ll know where to fetch the first instruction. We’ll call this control input, RESET
We’d also like RECOVERABLE INTERRUPTS for
FAULTS (eg, Illegal or unimplemented Instruction)
EXCEPTION GOAL: Interrupt running program, invoke exception handler, return to continue execution.
These are “Software”
notions of synchrony and asynchrony.
- CPU or SYSTEM generated [synchronous]
TRAPS & system calls (eg, read-a-character)
  CPU generated [synchronous, caused by an instruction]
(Implemented as an “agreed” upon Illegal instruction)
I/O events (eg, key press)
  externally generated [asynchronous]

## Slide 42: Exceptions
WA
PC
+4
A
Instruction Memory
D
Register File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
RD
WD R/W
Data Memory
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
32
PC+4
Rt: <20:16>
Imm: <15:0>
x4
+
BT
BT
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
PC<31:29>:J<25:0>:00
JT
JT
NV C Z
Rs: <25:21>
SEXT
BSEL
0
1
SEXT
5 4 3 2 1 0
0x80000000
0x80000040
0x80000080
PCSEL 6
RESET
 | IRQ Z N V C |  |  |  |  | 
Control Logic |  |  |  |  |  | 
Reset:
Bad Opcode: IRQ:
PC  0x80000000
Reg[27]  PC+4; PC  0x80000040 Reg[27]  PC+4; PC  0x80000080
These inputs should
probably be registered a few times to avoid metastability problems
ASEL
shamt:<10:6>
“16”
0 1 2
WASEL
Rd:<15:11> 0
WA
Rt:<20:16> 1
“31” 2
“27” 3

## Slide 43
This is a complete 32-bit processor. Although designed in one class lecture, it executes the majority of the
MIPS R2000 instruction set.
•Executes one instruction per clock
•All that’s left is the control logic design
WA
PC
+4
A
Instruction Memory
D
Register
File
RA1
RA2
RD1
RD2
ALU
A
B
WD WE
ALUFN
Control Logic
Data Memory
RD
WD
R/W
Adr
Wr
WDSEL
0 1 2
J:<25:0>
WERF
00
PC+4
Rt: <20:16>
Imm: <15:0>
+
x4
BT
BT
WASEL
Rd:<15:11> 0
WA
PCSEL WASEL
SEXT BSEL WDSEL
ALUFN
Wr
WERF ASEL
PC<31:29>:J<25:0>:00
JT
JT
N V C
NV C Z
Rs: <25:21>
ASEL
SEXT
BSEL
0
1
SEXT
shamt:<10:6>
5 4 3 2 1 0
“16”
IRQ Z
0x80000000
0x80000040
0x80000080
PCSEL 6
RESET
Rt:<20:16> 1
“31” 2
“27” 3
0 1 2

## Slide 44: 单周期完整设计-简化版
CS61C L221
Performance © UC Regents
计算机原理 L09 Single Cycle 1 (24)
imm16
32
ALUctr
Clk
busW
RegWr
32
32
busA
busB 32
Rw Ra Rb
32 32-bit Registers
Rt
Rs Rt
5 5 5
RegDst
Rd
Extender
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Data
32
In Clk | WrEn Adr Data Memory
MemWr
ALU
Equal
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rs Rt Rd
=
Adder
Adder
PC
Clk
00
Mux
4
PCSrc
PC Ext
Inst Memory
Adr

## Slide 45: Clock Distribution
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc
System Clock
clock cycle

## Slide 46: 小结
CPU设计直接决定了时钟周期宽度和CPI，所以对计算机性能非常重要！
CPU主要由数据通路和控制器组成
  数据通路：实现指令集中所有指令的操作功能
  控制器：控制数据通路中各部件进行正确操作
数据通路的两种元件
  操作元件(组合电路)：ALU、MUX、Ext.、Adder、Reg/Mem Read
  状态 / 存储元件(时序电路)：PC、Reg/Mem Write
数据通路的定时
  数据通路中操作元件没有存储功能，其操作结果须写到存储元件中
  在时钟到达后clk-to-Q时存储元件开始更新状态
MIPS指令集的一个子集作为CPU的实现目标
  公共操作：取指令和PC+4
  下址计算：32位PC,四路选择：顺序、Branch、Jump
  R型：ALU两个操作数来自rs和rt，结果写到rd
  访存：符号扩展，数据在rt和主存单元中交换
  立即数：0扩展后的操作数送到ALU的一个输入端

## Slide 47: 补充符号扩展问题Mips体系结构
ADDI和ADDIU的实现有以下2个要点：
1）仅支持有符号运算（补码运算），16位立即数需要进行符号扩展；
2）ADDI带有溢出检测（或者说带“自陷”功能，虽然不常用）。
ADDI和ADDIU的最大区别是有没有溢出标志（overflow）。
算术运算符号扩展
逻辑运算0扩展

## Slide 48: 单周期控制器的设计
考察每条指令在数据通路中的执行过程和涉及到的控制信号取值
  公共操作：取指令和计算下址PC
  R-Type指令(add / sub)
  立即数指令 (ori)
  访存指令(lw / sw)
  分支指令 (beq)
  跳转指令 (j)
汇总各指令的控制信号取值
  两类控制信号：直接送往数据通路 / 送往局部控制单元
分析ALU操作对应的控制信号与func字段间的关系
设计ALU局部控制单元
设计主控制单元

## Slide 49
控制器的设计
功能
给定一个指令字…
产生执行该指令所需的控制信号
实现方式：组合逻辑电路
输入信号
指令字段的op和func。
ALU的zero、V、N状态

## Slide 50
控制器的设计
确定每条指令的控制信号
0
1
X(与该指令无关)
构建控制信号的真值表

## Slide 51: Recap: Flexible Instruction Fetch
Branch (nPC_sel = “Br”):
  if (Equal == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
Other (nPC_sel = “+4”):
  PC=PC+4
What is encoding of nPC_sel?
  Direct MUX select?
  Branch / not branch
Let’s choose second option
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
imm16
Instruction<31:0>
0
1
Equal
nPC_MUX_sel
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 52: Recap: The Single Cycle Datapath during Add
32
ALUctr = Add or Sub
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = 1
Ext
Mux
Mux
32
16
imm16
ALUSrc = 0
ExtOp = x
Mux
MemtoReg = 0
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
R[rd] ← R[rs] + / - R[rt]
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
Notes: This picture shows the activities at the main datapath during the execution of the Add or Subtract instructions.
The active parts of the datapath are shown in different color as well as thicker lines.
First of all, the Rs and Rt of the instructions are fed to the Ra and Rb address ports of the register file and cause the contents of registers specified by the Rs and Rt fields to be placed on busA and busB, respectively.
With the ALUctr signals set to either Add or Subtract, the ALU will perform the proper operation and with MemtoReg set to 0, the ALU output will be placed onto busW.
The control we are going to design will also set RegWr to 1 so that the result will be written to the register file at the end of the cycle.
Notice that ExtOp is don’t care because the Extender in this case can either do a SignExt or ZeroExt. We DON’T care because ALUSrc will be equal to 0--we are using busB.
The other control signals we need to worry about are:
(a) MemWr has to be set to zero because we do not want to write the memory.
(b) And Branch and Jump, we have to set to zero. Let me show you why.

## Slide 53: Instruction Fetch for R-type Instruction
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 0
Zero = x
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
PC ← PC + 4
  All of the instructions except Branch and Jump are the same
Jump = 0
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
Notes: This picture shows the control signals setting for the Instruction Fetch Unit at the end of the Add or Subtract instruction.
Both the Branch and Jump signals are set to 0.
Consequently, the output of the first adder, which implements PC plus 1, is selected through the two 2-to-1 mux and got placed into the input of the Program Counter register.
The Program Counter is updated to this new value at the next clock tick.
Notice that the Program Counter is updated at every cycle. Therefore it does not have a Write Enable signal to control the write.
Also, this picture is the same for or all instructions other than Branch and Jump.
Therefore I will only show this picture again for the Branch and Jump instructions and will not repeat this for all other instructions.
+2 = 17 min. (X:57)

## Slide 54: Recap: The Single Cycle Datapath during Or Immediate
32
ALUctr = Or
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = 0
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 0
Mux
MemtoReg = 0
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
R[rt] ← R[rs] or ZeroExt[Imm16]
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
op
rs
rt
immediate
0
16
21
26
31
Notes: Now let’s look at the control signals setting for the Or immediate instruction.
The OR immediate instruction OR the content of the register specified by the Rs field to the Zero Extended Immediate field and write the result to the register specified in Rt.
This is how it works in the datapath. The Rs field is fed to the Ra address port to cause the contents of register Rs to be placed on busA.
The other operand for the ALU will come from the immediate field. In order to do this, the controller need to set ExtOp to 0 to instruct the extender to perform a Zero Extend operation.
Furthermore, ALUSrc must set to 1 such that the MUX will block off bus B from the register file and send the zero extended version of the immediate field to the ALU.
Of course, the ALUctr has to be set to OR so the ALU can perform an OR operation.
The rest of the control signals (MemWr, MemtoReg, Branch, and Jump) are the same as theAdd and Subtract instructions.
One big difference is the RegDst signal. In this case, the destination register is specified by the instruction’s Rt field, NOT the Rd field because we do not have a Rd field here.
Consequently, RegDst must be set to 0 to place Rt onto the Register File’s Rw address port.
Finally, in order to accomplish the register write, RegWr must be set to 1.
+3 = 20 min. (X:60)

## Slide 55: Recap: The Single Cycle Datapath during Load
32
ALUctr = Add
Clk
busW
RegWr = 1
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = 0
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 1
Mux
MemtoReg = 1
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
R[rt] ← Data Memory {R[rs] + SignExt[imm16]}
op
rs
rt
immediate
0
16
21
26
31
Notes: Let’s continue our lecture with the load instruction. What does the load instruction do?
It first adds the contents of the register specified by the Rs field to the Sign Extended version of the Immediate field to form the memory address.
Then it uses this memory address to access the memory and write the data back to the register specified by the Rt field of the instruction.
Here is how the datapath works: first the Rs field is fed to the Register File’s Ra address port to place the register onto bus A.
Then the ExtOp signal is set to 1 so that the immediate field is Sign Extended and we place this value (output of Extender) onto the ALU input by setting ALUsrc to 1.
The ALU then add (ALUctr = add) the two together to form the memory address which is then placed onto the Data Memory’s address port.
In order to place the Data Memory’s output bus onto the Register File’s input bus (busW), the control needs to set MemtoReg to 1.
Similar to the OR immediate instruction I showed you earlier, the destination register here is specified by the Rt field. Therefore RegDst must be set to 0.
Finally, RegWr must be set to 1 to complete the register write operation.
Well, it should be obvious to you guys by now that we need to set Branch and Jump to 0 to make sure the Instruction Fetch Unit update the Program Counter correctly.
+3 = 28 min. (Y:08)

## Slide 56: Recap: The Single Cycle Datapath during Store
32
ALUctr = Add
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = 1
ExtOp = 1
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 1
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
M{R[rs] + SignExt[imm16]} ← R[rt]
op
rs
rt
immediate
0
16
21
26
31
Notes: The store instruction performs the inverse function of the load. Instead of loading data from memory, the store instruction sends the contents of register specified by Rt to data memory.
Similar to the load instruction, the store instruction needs to read the contents of register Rs (points to Ra port) and add it to the sign extended verion of the immediate filed (Imm16, ExtOp = 1, ALUSrc = 1) to form the data memory address (ALUctr = add).
However unlike the Load instructoion where busB is not used, the store instruction will use busB to send the data to the Data memory.
Consequently, the Rt field of the instruction has to be fed to the Rb port of the register file.
In order to write the Data Memory properly, the MemWr signal has to be set to 1.
Notice that the store instruction does not update the register file. Therefore, RegWr must be set to zero and consequently control signals RegDst and MemtoReg are don’t cares.
And once again we need to set the control signals Branch and Jump to zero to ensure proper Program Counter updataing.
Well, by now, you are probably tied of these boring stuff where Branch and Jump are zero so let’s look at something different--the bracnh instruction.
+3 = 31 min. (Y:11)

## Slide 57: Recap: The Single Cycle Datapath during Branch
32
ALUctr = Sub
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = 0
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 0
Branch = 1
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
if (R[rs] - R[rt] == 0) then Zero ← 1 ; else Zero ← 0
op
rs
rt
immediate
0
16
21
26
31
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 58: Instruction Fetch for Branch Instruction
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 1
Zero = 1
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
Jump = 0
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
if (Zero == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the sequential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 59: Recap: The Single Cycle Datapath during Jump
32
ALUctr = x
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Ext
Mux
Mux
32
16
imm16
ALUSrc = x
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump = 1
Branch = 0
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
Send the JUMP address to PC without any additional operation!
op
target address
0
26
31
How to prevent the MEM and Reg writing ?
Notes: The control signals setting in the main datapath for the Jump instruction is pretty boring because in most cases, we DON’T CARE.
More specifically, control signals ExtOp, ALUSrc, ALUctr are all don’t cares because the ALU is not used at all for the Jump instruction.
Control signals MemtoReg and RegDst are don’t are because Jump does not write the register file. That is the reason why we still need to set RegWr to zero.
Furthermore, we also need to set MemWr to zero to avoid Data Memroy write.
Finally, the control signal Branch is set to zero but Jump is set to 1.
+2 = 37 min. (X:17)
Complement: So far as we have already seen, almost all instructions use ALU. But this jump instruction is exceptional.
which instruction doesn't use ALU?

## Slide 60: Instruction Fetch for Jump Instruction
30
30
SignExt
30
16
imm16
Mux
0
1
Adder
“1”
PC
Clk
Adder
30
30
Branch = 0
Zero = x
“00”
Addr<31:2>
Instruction
Memory
Addr<1:0>
32
Mux
1
0
26
4
PC<31:28>
Target
30
PC ← PC<31:29> concat target<25:0> concat “00”
Jump = 1
Instruction<15:0>
Instruction<31:0>
30
Instruction<25:0>
op
target address
0
26
31
Notes: Inside the Instruction Fetch Unit, with Branch set to zero and Jump set to 1, we will not use the output of neither Adder.
What we will use is the concatenation of the four most significant bits of the current program counter and the twenty six bits of the target address.
With the control signal Jump set to 1, this value will be send to the Program Counter and get written into PC at the next clock tick (points to the Clk bubble).
+2 = 39 min. (Y:19)
There should be an improvement: When Jump=1, we don’t have to set Branch=0. We can set Branch=x to simply logical design of the control part. But we have to set Jump=0 when Branch=1.

## Slide 61: Recap: A Summary of Control Signals
inst Register Transfer
ADD R[rd] <– R[rs] + R[rt]; PC <– PC + 4
ALUsrc = RegB, ALUctr = “add”, RegDst = rd, RegWr, nPC_sel = “+4”
SUB R[rd] <– R[rs] – R[rt]; PC <– PC + 4
ALUsrc = RegB, ALUctr = “sub”, RegDst = rd, RegWr, nPC_sel = “+4”
ORi R[rt] <– R[rs] + zero_ext(Imm16); PC <– PC + 4
ALUsrc = Im, Extop = “Z”, ALUctr = “or”, RegDst = rt, RegWr, nPC_sel = “+4”
LOAD R[rt] <– MEM[ R[rs] + sign_ext(Imm16)]; PC <– PC + 4
ALUsrc = Im, Extop = “Sn”, ALUctr = “add”, MemtoReg, RegDst = rt, RegWr, nPC_sel = “+4”
STORE MEM[ R[rs] + sign_ext(Imm16)] <– R[rs]; PC <– PC + 4
ALUsrc = Im, Extop = “Sn”, ALUctr = “add”, MemWr, nPC_sel = “+4”
BEQ if ( R[rs] == R[rt] ) then PC <– PC + sign_ext(Imm16)] || 00 else PC <– PC + 4
nPC_sel = “Br”, ALUctr = “sub”

## Slide 62: Assemble Control logic
ALUctr
RegDst
ALUSrc
ExtOp
MemtoReg
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
nPC_sel
Adr
Inst
Memory
DATA PATH
Decoder
Op
<21:25>
Fun
RegWr

## Slide 63
控制器：一个宠大的逻辑电路
好的方法：分成多个较小的逻辑电路
较小规模的逻辑电路速度更快
较小规模的逻辑电路更容易协同工作
显然
funct字段只与ALU的operation有关
好的方法：建立一个单独的ALU控制电路
控制器的设计

## Slide 64
建立一个单独的ALU控制电路
Operation
PCSrc
ALUSrc
MemWrite
MemRead
MemtoReg
RegDst
RegWrite
3
Control Unit
Datapath
Instruction
I
32
Operation
PCSrc
ALUSrc
MemWrite
MemRead
MemtoReg
RegDst
RegWrite
Zero
Zero
funct
op
I[31:26]
I[5:0]
6
6
6
aluop
aluop
2
nPC_sel

## Slide 65
控制器修改后的数据路径
5
5
16
RD1
RD2
RN1
RN2
WN
WD
RegWrite
Register File
Operation
ALU
4
E
X
T
N
D
16
32
Zero
RD
WD
MemRead
Data
Memory
ADDR
MemWrite
5
Instruction
I
32
M
U
X
ALUSrc
MemtoReg
ADD
<<2
RD
Instruction
Memory
ADDR
PC
4
ADD
ADD
M
U
X
M
U
X
PCSrc
MUX
RegDst
5
0
1
0
1
1
0
1
0
ALU
Control
Control
Unit
6
6
op I[31:
op
I[31:26]
funct
I[5:0]
ALUOp
2

## Slide 66
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
Add
1
0
0
1
0
0
0
x
Subtr
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtr
x
x
x
0
0
0
1
x
xxx
op
target address
op
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
10 0000
10 0010
We Don’t Care :-)
A Summary of the Control Signals
Ori rt,rs,imm
l
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something called “local decoding.”
+3 = 42 min. (Y:22)

## Slide 67: The Concept of Local Decoding
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUctr
1
0
0
1
0
0
0
x
Add/Subtr
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtr
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
func
Main
Control
op
6
ALU
Control
(Local)
N=?
6
ALUop
ALUctr
3
ALU
Two levels of decoding: Main Control and ALU Control
ALUctr is determined by ALUop and func, while other control signals are determined by op。
How many bits will N need?
R、I-ori、I-lw/sw、I-beq、J
3, why?
Notes: That is, instead of asking the Main Control to generates the ALUctr signals directly (see the diagram with the ALU), the main control will generate a set of signals called ALUop.
For all I and J type instructions, ALUop will tell the ALU Control exactly what the ALU needs to do (Add, Subtract, ...) .
But whenever the Main Control sees a R-type instructions, it simply throws its hands up and say: “Wow, I don’t know what the ALU has to do but I know it is a R-type instruction” and let the Local Control Block, ALU Control to take care of the rest.
Notice that this save us one column from the table we had on the last slide. But let’s be honest, if one column is the ONLY thing we save, we probably will not do it.
But when you have to design for the entire MIPS instruction set, this column will used for ALL R-type instructions, which is more than just Add and Subtract I showed you here.
Another advantage of this table over the last one, besides being smaller, is that we can uniquely identify each column by looking at the Op field only.
Therefore, as I will show you later, the Main Control ONLY needs to look at the Opcode field.
How many bits do we need for ALUop?
+3 = 45 min. (Y:25)

## Slide 68: The Decoding of the “func” Field
R-type
ori
lw
sw
beq
jump
ALUop (Symbolic)
“R-type”
Or
Add
Add
Subtr
xxx
ALUop<2:0>
1 xx
0 10
0 00
0 00
0x1
xxx
Main
Control
op
6
ALU
Control
(Local)
func
N
6
ALUop
ALUctr
3
000000
rs
rt
rd
shamt
func
0
6
11
16
21
26
31
R-type
func<5:0>
Instruction Operation
10 0000
10 0010
10 0100
10 0101
10 1010
add
subtract
and
or
set-on-less-than
ALUctr<2:0>
ALU Operation
000
001
100
101
010
Add
Subtract
And
Or
Subtract
ALUctr
ALU
Encoding ALUop as follows
Could ALUop use just 2 bits？
Yes！Since jump is X，we could use 2 bits：R:11, I-ori:10, I-beq:01, I-lw/sw:00, J-xx
R-Type is1xx，could identify R-instruction by using 1 bit！
Notes: What this table and diagram implies is that if the ALU Control receives ALUop = 100, it has to decode the instruction’s “func” field to figure out what the ALU needs to do.
Based on the MIPS encoding in Appendix A of your text book, we know we have a Add instruction if the func field is 10 000.
If the func field is 10 0010, we know we have a subtract operation and so on.
Notice that the bit 5 and bit 4 of this field is the same for all these operations so as far as the ALU control is concerned, these bits are don’t care.
Now recall from your ALU homework, the ALUctr signals has the following meaning (point to the table): 000 means Add, 001 means subtract, ... etc.
Based on these three tables (point to the last row of the top table and then the two other tables) and the fact that bit 5 and bit 4 of the “func” field are don’t care, we can derive the following truth table for ALUctr.
+2 = 48 min. (Y:28)

## Slide 69: The Truth Table for ALUctr
R-type
ori
lw
sw
beq
ALUop
(Symbolic)
“R-type”
Or
Add
Add
Subtr
ALUop<2:0>
1 00
0 10
0 00
0 00
0 x1
ALUop
func
bit2
bit1
bit0
bit<2>
bit<1>
bit<0>
bit<3>
0
0
0
x
x
x
x
ALUctr
ALU
Operation
Add
0
0
0
bit<2>
bit<1>
bit<0>
0
x
1
x
x
x
x
Subtract
0
0
1
0
1
0
x
x
x
x
Or
1
1
0
1
x
x
0
0
0
0
Add
0
0
0
1
x
x
0
0
1
0
Subtract
0
0
1
1
x
x
0
1
0
0
And
0
1
0
1
x
x
0
1
0
1
Or
1
1
0
1
x
x
1
0
1
0
Subtract
0
0
1
funct<3:0>
Instruction Op.
0000
0010
0100
0101
1010
add
subtract
and
or
set-on-less-than
Non-R-type Instructions
determined by ALUop
R-type Instructions
determined by funct
Notes: That is, whenever ALUop is 000, we don’t care anything about the func field because we know we need the ALU to do an ADD operation (point to Add column).
Whenever the ALUop bit<2> is 0 and bit<0> is 1, we know we want the ALU to perform a Subtract regardless of what func field is.
Bit<1> is a don’t care because for our encoding here, ALUop<1> will never be equal to 1 whenever bit<0> is 1 and bit<2> is 0.
Similarly, whenever ALUop bit<2> is 0 and bit<1> is 1, we need the ALU to perform Or.
The tricky part occurs when the ALUOp bit<2> equals to 1. In that case, we have a R-type instruction and we need to look at the Func field.
In any case, once we have this Symbolic column, we can get this actual bit columns by referring to our ALU table on the last slide (use the last table of last slide if time permits).
+2 = 30 min. (Y:30)

## Slide 70: The Logic Equation for ALUctr<0>
ALUctr<0> = !ALUop<2> & ALUop<0> +
  ALUop<2> & !func<2> & func<1> & !func<0>
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
ALUctr<0>
0
x
1
x
x
x
x
1
1
x
x
0
0
1
0
1
1
x
x
1
0
1
0
1
This makes func<3> a don’t care
Choose the rows with ALUctr[0]=1
Notes: From the truth table we had before the break, we can derive the logic equation for ALUctr bit 2 by collecting all the rows that has ALUCtr bit 2 equals to 1 and this table is the result.
Each row becomes a product term and we need to OR the product terms together.
Notice that the last row are identical except the bit<3> of the func fields. One is zero and the other is one. Together, they make bit<3> a don’t care term.
With all these don’t care terms, the logic equation is rather simple.
The first product term is: not ALUOp<2> and ALUOp<0>.
The second product term, after we making Func<3> a don’t care becomes ...
+2 = 57 min. (Y:37)

## Slide 71: The Logic Equation for ALUctr<1>
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
0
1
0
x
x
x
x
1
ALUctr<1>
1
x
x
0
1
0
0
1
1
x
x
0
1
0
1
1
ALUctr<1> = !ALUop<2> & ALUop<1> & ! ALUop<0> +
  ALUop<2> & !func<3> & func<2> & !func<1>
Choose the rows with ALUctr[1]=1
Notes: Here is the truth table when we collect all the rows where ALCctr bit<1> equals to 1.
Once again, we can simplify the table by noticing that the first two rows are different only at the ALUop bit<0> position. We can make ALUop bit<0> into a don’t care.
Similarly, the last three rows can be combined to make Func bit<3> and bit<1> into don’t cares. I cannot understand it.
Consequently, the logic equation for ALUctr bit<1> becomes ...
+2 = 59 min. (Y:39)

## Slide 72: The Logic Equation for ALUctr<2>
ALUop
func
bit<2>
bit<1>
bit<0>
bit<2>
bit<1>
bit<0>
bit<3>
ALUctr<2>
0
1
0
x
x
x
x
1
1
x
x
0
1
0
1
1
ALUctr<2> = !ALUop<2> & ALUop<1> & !ALUop<0>
  + ALUop<2> & !func<3> & func<2> & !func<1> & func<0>
Choose the rows with ALUctr[2]=1
Notes: Finally, after we gather all the rows where ALUctr bit 0 are 1’s, we have this truth table.
Well, we are out of luck here. I don’t see any simple way to simplify these product terms by just looking at them.
There may be some if you draw out the 7 dimension K map but I am not going to try it.
So I just write down the logic equations as it is.
+2 = 61 min. (Y:41)

## Slide 73: Summery of Control Logic of Local Control
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
ALUctr<0> = !ALUop<2> & ALUop<0> +
  ALUop<2> & !func<2> & func<1> & !func<0>
ALUctr<1> = !ALUop<2> & ALUop<1> & !ALUop<0> +
  ALUop<2> & !func<3> & func<2> & !func<1>
ALUctr<2> = !ALUop<2> & ALUop<1> & !ALUop<0> +
  ALUop<2> & !func<3> & func<2> & !func<1> & func<0>
assign ALUctr<0> = !ALUop[2] & ALUop[0] +
  ALUop[2] & !func[2] & func[1] & !func[0];
assign Ctrl[1] = !ALUop[2] & ALUop[1] & !ALUop[0] +
  ALUop[2] & !func[3] & func[2] & !func[1] ;
assign Ctrl[2] = !ALUop[2[ & ALUop[1] & !ALUop[0] +
  ALUop[2] & !func[3] & func[2] & !func[1] & func[0]
endmodule
module ALUctrl(ALUop, func ,Ctrl);
input [3:0] ALUop;
input [3:0] func;
output [2:0] ALUctrl;
Notes: With all the logic equations available, you should be able to implement this logic block without any problem.
+1 = 62 min. (Y:42)

## Slide 74: The “Truth Table” for the Main Control
R-type
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
Branch
Jump
ExtOp
ALUop (Symbolic)
1
0
0
1
0
0
0
x
“R-type”
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtr
x
x
x
0
0
0
1
x
xxx
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
ALUop <2>
1
0
0
0
0
x
ALUop <1>
x
1
0
0
x
x
ALUop <0>
x
0
0
0
1
x
Main
Control
op
6
ALU
Control
(Local)
func
3
6
ALUop
ALUctr
3
RegDst
ALUSrc
:
Input of main control
Output of Main Control
Notes: Now that we have taken care of the Local Control (ALU Control), let’s refocus our attention to the Mian Controller.
The job of the Main Control is to look at the Opcode field of the instruction and generate these control signals for the datapath (RegDst, ... ExtOp) as well as the 3-bit ALUop field for the ALU Control.
Here, I have shown you the symbolic value of the ALUop field as well as the actual bit assignment.
For example here (2nd column), the R-type ALUop is encode as 100 and the Add operation (3rd column) is encoded as 000..
This is call a quote “Truth Table” unquote because if you think about it, this is like having the truth table rotates 90 degrees.
Let me show you what I mean by that.
+3 = 65 min. (Y:45)

## Slide 75: The “Truth Table” for RegWrite
R-type
ori
lw
sw
beq
jump
RegWrite
1
1
1
0
0
0
op
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
RegWrite = R-type + ori + lw
  = !op<5> & !op<4> & !op<3> & !op<2> & !op<1> & !op<0> (R-type)
  + !op<5> & !op<4> & op<3> & op<2> & !op<1> & op<0> (ori)
  + op<5> & !op<4> & !op<3> & !op<2> & op<1> & op<0> (lw)
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
Decoder
Notes: For example, consider the control signal RegWrite.
If we treat all the don’t cares as zeros, this row here means RegDest has to be equal to one whenever we have a R-type, or an OR immediate, or a load instruction.
Since we can determine whether we have any of these instructions (point to the column headers) by looking at the bits in the “OP” field, we can transform this symbolic equation to this binary logic equation.
For example, the first product term here say we have a R-type instruction whenever all the bits in the “OP” field are zeros.
So each of these big AND gates implements one of the columns (R-type, ori, ...) in our table. Or in more technical terms, each AND gate implements a product term.
In order to finish implementing this logic equation, we have to OR the proper terms together.
In the case of the RegWrite signal, we need to OR the R-type, ORi, and load terms together.
+2 = 67 min. (Y:47)

## Slide 76: The “Truth Table” for RegWrite
op<0>
op<5>
.
.
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
op<5>
.
.
<0>
R-type
ori
lw
sw
beq
jump
RegWrite
ALUSrc
MemtoReg
MemWrite
Branch
Jump
RegDst
ExtOp
ALUop<2>
ALUop<1>
ALUop<0>
Decoder
Notes: Similarly, for ALUSrc, we need to OR the ori, load, and store terms together because we need to assert the ALUSrc signals whenever we have the Ori, load, or store instructions.
The RegDst, MemtoReg, MemWrite, Branch, and Jump signals are very simple. They don’t need to OR any product terms together because each is asserted for only one instruction.
For example, RegDst is asserted ONLY for R-type instruction and MemtoReg is asserted ONLY for load instruction.
ExtOp, on the other hand, needs to be set to 1 for both the load and store instructions so the immediate field is sign extended properly.
Therefore, we need to OR the load and store terms together to form the signal ExtOp.
Finally, we have the ALUop signals.
But clever encoding of the ALUop field, we are able to keep them simple so that no OR gates is needed.
If you don’t already know, this regular structure with an array of AND gates followed by another array of OR gates is called a Programmable Logic Array, or PLA for short.
It is one of the most common ways to implement logic function and there are a lot of CAD tools available to simplify them.
+3 = 70 min. (Y:50)

## Slide 77: The Complete Single Cycle Data Path with Control
32
ALUctr
Clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst
Ext
Mux
Mux
32
16
imm16
ALUSrc
ExtOp
Mux
MemtoReg
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
Jump
Branch
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
Main
Control
op
6
ALU
Control
func
6
3
ALUop
ALUctr
3
RegDst
ALUSrc
:
Instr<5:0>
Instr<31:26>
Instr<15:0>
Notes: OK, now that we have the Main Control implemented, we have everything we needed for the single cycle processor and here it is.
The Instruction Fetch Unit gives us the instruction. The OP field is fed to the Main Control for decode and the Func field is fed to the ALU Control for local decoding.
The Rt, Rs, Rd, and Imm16 fields of the instruction are fed to the data path.
Based on the OP field of the instruction, the Main Control will set the control signals RegDst, ALUSrc, .... etc properly as I showed you earlier using separate slides.
Furthermore, the ALUctr use the ALUop from the Main control and the func field of the instruction to generate the ALUctr signals to ask the ALU to do the right thing: Add, Subtract, Or, and so on.
This processor will execute each of the MIPS instruction in the subset in one cycle.
There is, however, a couple of subtle differences between this single-cycle processor and a real MIPS processor in terms of instruction execution.
+2 = 72 min (Y:52)

## Slide 78: Time Delay for LW: Critical Path
Clk
PC
Rs, Rt, Rd,
Op, Func
Clk-to-Q
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA
Register File Access Time
Old Value
New Value
busB
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
ExtOp
Old Value
New Value
ALUSrc
Old Value
New Value
MemtoReg
Old Value
New Value
Address
Old Value
New Value
busW
Old Value
New
Delay through Extender & Mux
Register
Write Occurs
Data Memory Access Time
PC+4
PC+4 PC
Notes: This timing diagram shows the worst case timing of our single cycle datapath which occurs at the load instruction.
Clock to Q time after the clock tick, PC will present its new value to the Instruction memory.
After a delay of instruction access time, the instruction bus (Rs, Rt, ...) becomes valid.
Then three things happens in parallel:
(a) First the Control generates the control signals (Delay through Control Logic).
(b) Secondly, the register file access is to put Rs onto busA.
(c) And we have to sign extended the immediate field to get the second operand (busB).
Here I assume register file access takes longer time than doing the sign extension so we have to wait until busA valid before the ALU can start the address calculation (ALU delay).
With the address ready, we access the data memory and after a delay of the Data Memory Access time, busW will be valid.
And by this time, the control unit would have set the RegWr signal to one so at the next clock tick, we will write the new data coming from memory (busW) into the register file.
+3 = 77 min. (Y:57)

## Slide 79: Time Delay for R型指令: Critical Path

## Slide 80
单周期CPU的性能
假设各部件延时如下：
存储读/写：200ps
ALU、加法器：100ps
寄存器堆读/写：50ps
控制器 -忽略不计：0ps
选择器-忽略不计：0ps
各种指令的执行所需的指令周期是多少？

## Slide 81
R型指令
200ps
100ps (not on critical path)
100ps
50ps
50ps
Longest Path:
200ps
+ 50ps
+ 100ps
+ 50ps
400ps

## Slide 82
Lw指令
200ps
100ps (not on critical path)
100ps
50ps
50ps
Longest Path:
200ps
+ 50ps
+ 100ps
+ 200ps
+ 50ps
600ps
200ps

## Slide 83
Sw指令
200ps
100ps (not on critical path)
100ps
50ps
Longest Path:
200ps
+ 50ps
+ 100ps
+ 200ps
550ps
200ps

## Slide 84
分支指令
200ps
100ps (not on critical path)
100ps
50ps
Longest Path:
200ps
+ 50ps
+ 100ps
350ps

## Slide 85: What’s wrong with our CPI=1 processor?
PC
Inst Memory
mux
ALU
Data Mem
mux
PC
Reg File
Inst Memory
mux
ALU
mux
PC
Inst Memory
mux
ALU
Data Mem
PC
Inst Memory
cmp
mux
Reg File
Reg File
Reg File
Arithmetic & Logical
Load
Store
Branch
Critical Path
setup
setup
The critical path is the path to get the data for a load instruction, so we have I-Mem, Regs, Mux, ALU, D-Mem, and Mux ， RegWrite on this path.
Clock-to-Q-time:在触发时钟边沿，输出并不能立即变化，如果比较大时也要考虑进去
切记：状态单元的输入信息总是在一个时钟边沿到达后的“Clk-to-Q”时才被写入到单元中，此时的输出才反映新的状态值

## Slide 86: Single Cycle Implementation Cycle Time
Unfortunately, though simple, the single cycle approach is not used because it is very slow
Clock cycle must have the same length for every instruction
What is the longest (slowest) path (slowest instruction)?
  单周期设计中时钟周期对所有的指令等长，因此要由计算机中可能的最长路径决定：
——取指令
违反了设计原则 —— 加速完成常用操作

## Slide 87: Instruction Critical Paths
Instr. | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type |  |  |  |  |  | 
load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
Calculate cycle time assuming negligible delays (for muxes, control unit, sign extend, PC access, shift left 2, wires) except:
  Instruction and Data Memory (4 ns)
  ALU and adders (2 ns)
  Register File access (reads or writes) (1 ns)
Notes: For class handout

## Slide 88: Instruction Critical Paths
Instr. | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type |  |  |  |  |  | 
load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
4 | 1 | 2 |  | 1 | 8
4 | 1 | 2 | 4 | 1 | 12
Calculate cycle time assuming negligible delays (for muxes, control unit, sign extend, PC access, shift left 2, wires, setup and hold times) except:
  Instruction and Data Memory (4 ns)
  ALU and adders (2 ns)
  Register File access (reads or writes) (1 ns)
4 | 1 | 2 | 4 |  | 11
4 | 1 | 2 |  |  | 7
4 |  |  |  |  | 4
Notes: For lecture
Note that PC is updated during I Mem read

## Slide 89: Single Cycle Disadvantages & Advantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instr
  especially problematic for more complex instructions like floating point multiply
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
but
It is simple and easy to understand
Clk
lw
sw
Waste
Cycle 1
Cycle 2
Notes: In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.

## Slide 90
单周期CPU的性能
各类指令的数据路径长度
R型指令 200 + 50 + 100+0+50 400ps
Load word 200 + 50 + 100 + 200 + 50 600ps
Store word 200 + 50 + 100 + 200 550ps
  分支 200 + 50 + 100 350ps
  转移 200 200ps
  性能受最慢指令的限制

## Slide 91: 单周期计算机的性能
假设在单周期处理器中，各主要功能单元的操作时间为：
存储单元：200ps
ALU和加法器：100ps
寄存器堆（读/写）：50ps
假设程序中各类指令占比：25%取数、10%存数、45%ALU、15%分支、5%跳转
假设MUX、控制单元、PC、扩展器和传输线路都没有延迟，则下面实现方式中，哪个更快？快多少？
（1）每条指令在一个固定长度的时钟周期内完成
（2）每条指令在一个时钟周期内完成，但时钟周期仅为指令所需，也即为可变的（实际不可行，只是为了比较）

## Slide 92: 单周期计算机的性能
解：CPU执行时间=指令条数 x CPI x 时钟周期=指令条数 x 时钟周期
两种方案的指令条数都一样，CPI都为1，所以只要比较时钟周期宽度即可。
各类指令要求的时间长度为：

## Slide 93: 单周期计算机的性能
对于方式（1），时钟周期由最长指令来决定，应该是load指令，为600ps
对于方式（2），时钟周期取各条指令所需时间，时钟周期从600ps至200ps不等
根据各类指令的频度，计算出平均时钟周期长度为：
CPU时钟周期=600x25%+550x10%+400x45%+350x15%+200x5%=447.5ps
CPU性能比= = = =1.34
方式(1)的CPU执行时间
方式(2)的CPU执行时间
方式(1)的CPU 时钟周期
方式(2)的CPU 时钟周期
600
447.5
由此可见，可变时钟周期的性能是定长周期的1.34倍
但是，对每类指令采用可变长时钟周期实现非常困难，而且所带来的额外开销会很大，不合算！
早期的小指令集计算机用过单周期实现技术，但现代计算机都不采用。

## Slide 94: 单周期计算机的性能
单周期计算机的性能练习：
假设各主要功能单元的操作时间为：
    读存储器：10ns，写存储器：5ns
    ALU和加法器：10ns
    寄存器堆（读/写）：5ns
而MUX、控制单元、PC、扩展器和传输线路没有延迟，若各类指令的执行次数占总数的比例为：20%取数、10%存数、50%ALU、15%分支、5%跳转，则下面实现方式中，哪个更快？快多少？
    每条指令在一个固定长度的时钟周期内完成
    每条指令在一个时钟周期内完成，但时钟周期是可以根据指令类型动态变化的。

## Slide 95: 单周期计算机的性能
    解：方式(1)：时钟周期由最长指令来决定，应是load指令，为 40ns——Load指令的执行如下：
    取指令10ns,读寄存器堆5ns，ALU计算地址10ns,读存储器10ns,写寄存器堆5ns,总的时间是40 ns。
方式(2)：时钟周期取各条指令所需时间，根据各类指令的频度，计算出平均时钟周期为：
    30×50% ＋ 40×20% ＋ 35×10% ＋25×15% +10 ×5% = 30.75ns
加速比=可变周期处理机的性能/固定周期处理机的性能
= (I ×1×40) / (I ×1 ×30.75 ) = 1.3
可变周期处理机的性能是固定周期处理机性能的1.3倍！

## Slide 96: MIPS Control
The control unitt can be implemented using a ROM
Insttructtion | R E S E T | I R Q | Z | N | V | C | P C S E L | S E X T | W A S E L | W D S E L | ALUFN Sub Bool Shftt Matth |  |  |  | W R | W E R F | A S E L | B S E L
--- | 1 | X | X | X | X | X | 4 | 0 | 0 | 0 | 0 | 00 | 0 | 0 | 0 | 0 | 0 | 0
--- | 0 | 1 | X | X | X | X | 6 | 0 | 3 | 0 | 0 | 00 | 0 | 0 | 0 | 0 | 0 | 0
add | 0 | 0 | X | X | 0 | X | 0 | 0 | 0 | 1 | 0 | 00 | 0 | 1 | 0 | 1 | 0 | 0
sll |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
andi |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw | 0 | 0 | X | X | X | X | 0 | 1 | 1 | 2 | 0 | XX | 0 | 1 | 0 | 1 | 0 | 1
sw | 0 | 0 | X | X | X | X | 0 | 1 | X | X | 0 | XX | 0 | 1 | 1 | 0 | 0 | 1
beq | 0 | 0 | 0 | X | X | X | 0 | 1 | X | X | 1 | XX | 0 | 1 | 0 | 0 | 0 | 0
beq | 0 | 0 | 1 | X | X | X | 1 | 1 | X | X | 1 | XX | 0 | 1 | 0 | 0 | 0 | 0
lui |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 97
其它可实现的方式
多周期处理器
缩短指令周期
一条指令多个周期
  不同类型指令所需的周期数不同
  硬件代价小
  流水线处理
  指令重叠执行
  尽可缩短时钟周期数和CPI
  硬件代价大，但性能更好