## Slide 1: What’s wrong with our CPI=1 processor?
PC
Inst Memory
mux
ALU
Data Mem
mux
PC
Reg File
Inst Memory
mux
ALU
mux
PC
Inst Memory
mux
ALU
Data Mem
PC
Inst Memory
cmp
mux
Reg File
Reg File
Reg File
Arithmetic & Logical
Load
Store
Branch
Critical Path
setup
setup
Performance of Single-Cycle Machine
  An implementation in which every instruction operates in 1 clock cycle of a fixed length.

## Slide 2: Multicycle Implementation Overview
Each instruction step takes 1 clock cycle
  Therefore, an instruction takes more than 1 clock cycle to complete
Not every instruction takes the same number of clock cycles to complete
Multicycle implementations allow
  更快的时钟频率
  不同的指令用不同的周期数
  单个ALU用于所有计算
  单个存储器用于指令和数据的存储
  需要增加寄存器暂存数据用于跨时钟周期

## Slide 3: The Multicycle Datapath – A High Level View
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
Registers have to be added after every major functional unit to hold the output value until it is used in a subsequent clock cycle
Notes: Note extra registers added – IR, MDR, A, B, and ALUout

## Slide 4: Clocking the Multicycle Datapath
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
System Clock
MemWrite
RegWrite
clock cycle
Notes: Note extra registers added – IR, MDR, A, B, and ALUout

## Slide 5: Our Multicycle Approach
Break up the instructions into steps where each step takes a clock cycle while trying to
  balance the amount of work to be done in each step
  use only one major functional unit per clock cycle
At the end of a clock cycle
  Store values needed in a later clock cycle by the current instruction in a state element (internal register not visible to the programmer)
    IR – Instruction Register
    MDR – Memory Data Register
    A and B – Register File read data registers
    ALUout – ALU output register
    All (except IR) hold data only between a pair of adjacent clock cycles (so they don’t need a write control signal)
  Data used by subsequent instructions are stored in programmer visible state elements (i.e., Register File, PC, or Memory)

## Slide 6: The Complete Multicycle Data with Control
Address
Read Data
(Instr. or Data)
Memory
PC
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
Write Data
IR
MDR
A
B
ALUout
Sign
Extend
Shift
left 2
ALU
control
Shift
left 2
ALUOp
Control
IRWrite
MemtoReg
MemWrite
MemRead
IorD
PCWrite
PCWriteCond
RegDst
RegWrite
ALUSrcA
ALUSrcB
zero
PCSource
1
1
1
1
1
1
0
0
0
0
0
0
2
2
3
4
Instr[5-0]
Instr[25-0]
PC[31-28]
Instr[15-0]
Instr[31-26]
32
28
Notes: For class handout

## Slide 7: 考察每条指令在单周期数据通路中的执行过程
  每条指令在一个时钟周期内完成
  每个时钟到来时，都开始进入取指令操作
    经过clk-to-Q，PC得到新值，经过access time后得到当前指令
    按三种方式分别计算下条指令地址，在branch / zero / jump的控制下，选择其中之一送到PC输入端，但不会马上写到PC中，一直到下个时钟到达时，才会更新PC。三种下址方式为：
      branch=jump=0：PC+4
      branch=zero=1： PC+4+signExt[imm16]*4
      jump=1： PC<31:28> concat target<25:0> concat “00”
  指令取出后被译码，产生指令对应的控制信号
    R-type指令：rd为目的寄存器，无访存操作，……
    ori指令：rt为目的寄存器，0扩展，无访存操作，……
    lw指令： rt为目的寄存器，计算地址、符号扩展，读内存，……
    sw指令： rt为源寄存器，计算地址、符号扩展，写内存，……
汇总每条指令控制信号的取值，生成真值表，写出逻辑表达式，设计主控制逻辑和ALU局部控制逻辑

## Slide 8: 单周期数据通路的缺点：回顾 Load 指令执行
Clk
5
Rw
Ra
Rb
32 32-bit
Registers
Rd
ALU
Clk
DataIn
DataOut
Data
Address
Ideal
Data
Memory
Instruction bus
Instruction Address
Ideal
Instruction
Memory
Clk
PC
5
Rs
5
Rt
16
Imm
32
32
32
32
单周期处理器的CPI为1，时钟周期以最长的load指令为准，时钟周期远远大于其他指令实际所需的执行时间，效率极低
  R-type指令、立即数运算指令不需要读内存
  Store指令不需要写寄存器
  分支指令不需要访问内存和写寄存器
  Jump 不需要ALU运算、读内存、读/写寄存器

## Slide 9: 多周期处理器的实现思想
解决思路:
  把指令的执行分成多个阶段，每个阶段在一个时钟周期内完成
    时钟周期以最复杂阶段所花时间为准
    尽量分成大致相等的若干阶段
    规定每个阶段最多只能完成1次访存 或 寄存器堆读/写 或 ALU
  每步都设置存储元件，每步执行结果都在下个时钟开始保存到相应单元
多周期处理器的好处:
  时钟周期短
  不同指令所用周期数可以不同，可参考：
  允许功能部件在一条指令执行过程中被重复使用。如：
    Adder + ALU（多周期时只用一个ALU，在不同周期可重复使用）
    Inst. / Data mem（多周期时合用，不同周期中重复使用）
Notes: Well, the root of these problems of course is that fact that the Single Cycle Processor’s cycle time has to be long enough for the slowest instruction.
The solution is simple. Just break the instruction into smaller steps and instead of executing an entire instruction in one cycle, we will execute each of these steps in one cycle.
Since the cycle time in this case will be the time it takes to execute the longest step, our goal should be keeping all the steps to have similar length when we break up the instruction.
Well the last two bullets pretty much summarize what a multiple cycle processor is all about.
The first advantage of the multiple cycle processor is of course shorter cycle time. The cycle time now only has to be long enough to execute the longest step.
But may be more importantly, now different instructions can take different number of cycles to complete. For example:
(1) The load instruction will take five cycles to complete.
(2) But the Jump instruction will only take three cycles.
This feature greatly reduce the idle time inside the processor.
Finally, the multiple cycle implementation allows a functional unit to be used more than once per instruction as long as it is used on different clock cycles.
For example, as I will show you later in today’s lecture, we can use the ALU to increment the Program Counter as well as doing address calculation.
+3 = 11 min. (X:51)

## Slide 10: 指令各阶段分析
取指令阶段
  执行一次存储器读操作
  读出的内容（指令）保存到寄存器IR（指令寄存器）中
  IR的内容不是每个时钟都更新，所以IR必须加一个“写使能”控制
  在取指令阶段结束时，ALU的输出为PC+4，并送到PC的输入端，但不能在每个时钟到来时就更新PC，所以PC也要有“写使能”控制
译码/读寄存器堆阶段
  经过控制逻辑延迟后，控制信号更新为新值
  执行一次寄存器读操作，并同时进行译码
  期间ALU空闲，可以考虑“投机计算”分支地址
ALU运算阶段
  ALU运算，输出结果一定要在下个时钟到达之前稳定
  如果是分支branch指令，该阶段需决定是否将分支地址写入PC
读存储器阶段
  由ALU运算结果作为地址访问存储器，读出数据
写结果到寄存器
  把之前的运算结果或读存储器结果写到寄存器堆中
第一个周期（取值周期）
第二个周期
（译码取数周期）
第三、四、五个周期（各指令不同）

## Slide 11: 寄存器堆和存储器的写定时（ Ideal vs. Reality）
单周期机器中，寄存器组和存储器被简化为理想的：
  时钟边沿到来之前，地址、数据和写使能都已经稳定
  时钟边沿到来时，才进行写
实际机器中，寄存器组和存储器的情况为：
  写操作不是由时钟边沿触发，是组合电路，其过程为：
    写使能(WE)为 1，并且 Din信号已稳定的前提下，经过Write Access时间，Din信号被写入 Adr 处
  重要之处: 地址和数据必须在写使能为1前稳定
Adr
Din
WrEn
Dout
Ideal
Memory
32
32
32
Clk
Adr
Din
WrEn
Dout
Real
Memory
32
32
32
因此，存在地址Adr、数据Din和写使能WrEn信号的“竞争”问题！
Notes: Because in a real register file, there is NO clock input (use the bottom picture).
In previous lectures, I tried to simplify things by giving both the register file and data memory a clock input such that all write happens at the clock tick-that is H to L transition of the clock.
Consequently, the address bus, the Data In bus, and the Write Enable signals must ALL be stable at least ONE set up time before the clock tick.
But in real life, neither register file nor ideal data memory has clock input.
The Write path is pure combinational. That is after the control signal:
(1) Write Enable has gone to 1 and the Data In bus has settle down to a given value.
(2) It will take a delay equal to the Memory Write Access Delay.
(3) BEFORE the value on the Data In bus is written into the memory location
specified by the address bus.
It is very VERY important that the address bus is stable BEFORE the control signal Write Enable is set to 1.
Otherwise, you may end up destroying data already in memory by writing to the wrong address location if there is any glitches on the address bus when Write Enable is asserted.
+2 = 15 min. (X:55)

## Slide 12: 竞争（race）问题
Register File(寄存器组)：
  不能保证 Rw 和busW在RegWr = 1之前稳定
  即在 Rw和busW 与RegWr 之间存在“race”
Memory(存储器)：
  不能保证 Adr和Din在WrEn = 1之前稳定
  即：在 Adr 和Din与 WrEn之间存在“race”
Reg File
Ra
Rw
busW
Rb
busA
busB
RegWr
5
5
5
32
32
32
Adr
Din
WrEn
Dout
Real
Memory
32
32
32
“Race”问题有时会导致机器神秘出错，甚至崩溃！
Notes: Notice that this real register file, which does not have a clock input, may not work reliably in our single cycle processor because if you look at the timing diagram, you will notice that:
(1) We cannot guarantee Rw, which specifies the register to be written, will be stable
BEFORE the control signal RegWr goes to 1.
(2) In other words we have a race between the setting of Rw and the assertion of RegWr.
On a good day, if Rw does settle down before RegWr goes to 1, everything works. But once in a while, if RegWr happens to go to 1 before Rw settles down, we have a problem.
Race condition like this is what caused machine to crash mysteriously during initial testing.
Similarly, I did not use this data memory in our single cycle processor design because we cannot guarantee the address bus to be stable BEFORE Write Enable is set to 1.
Once again, we have a race condition between the Address and the Write Enable signal.
How can we avoid these two race conditions in our multiple cycle implementation?
+2 = 17 min. (X:57)

## Slide 13: 如何在多周期通路中避免“race”问题
多时钟周期中解决“竞争”问题的方案
  确认地址和数据在第N周期结束时已稳定
  使写使能信号在一个周期后(即：第N+1周期)有效
  在写使能信号无效前地址和数据不改变
Reg File
Ra
Rw
busW
Rb
busA
busB
RegWr
5
5
5
32
32
32
Adr
Din
WrEn
Dout
Real
Memory
32
32
32
Notes: Well, for the multiple cycle implementation, we can avoid this race condition by:
(1) Making sure the address bus is stable by the end of Cycle N.
(2) Then we can assert the write enable signal ONE cycle later at Cycle N + 1.
(3) Finally, we have to make sure the address bus does not change until the
Write Enable signal is disasserted.
+1 = 18 min. (X:18)

## Slide 14: 取指周期（取指令、计算下地址）开始时
在一个时钟到来的下降沿开始取指令周期的任务：
  M[PC] ； PCPC + 4
Real
Memory
Din
Adr
32
32
32
Dout
MemWr=0
PC
32
32
Clk
ALU
32
32
ALUop=add
ALU
Control
4
I R
32
Clk
IRWr=1
PCWr=1
Clk
You are here!
One “Logic” Clock Cycle
PC和IR怎样在必要时更新？
加“写使能”控制！
Notes: As far as LOGIC is concerned, I think the easiest way to think about a clock cycle is that a clock cycle begins right AFTER a clock tick and ends at the next clock tick.
I have intentionally shown the L time to be much longer than the H time to emphasis a point: the H and L time does not affect your design as long as you use the simple clocking methodology where all storage elements are triggered at the same clock tick.
The only important thing here is the time between the two clock ticks, the cycle time.
Most of the time, however, the high and low time are the same because it is much easier to generate a clock that has high and low time the same length. Well enough about clock ticks.
Let’s see what happens at the beginning (You are Here) of the Ifetch cycle:
(a) We need to fetch the instruction from Memory so we sent the address to the memory.
(b) We also needs to update the PC so we better send the address to the ALU as well.
***** What values do you think the control signals PCwr and ALUop have at this point?
Well since we are only at the beginning of the cycle (Your are Here), these two signals will still have the old values from the last cycle of the previous value. See next slide of their new values.
+2 = 27 min. (Y:07)

## Slide 15: 取指周期结束时
每一个周期都在下一个时钟到来时结束 (此时，受时钟控制的存储元件被更新。不受时钟约束的存储原件则没有此特点):
  IR  M[PC] PC  PC + 4
Real
Memory
Din
Adr
32
32
32
Dout
MemWr=0
PC
32
32
Clk
ALU
32
32
ALUOp = Add
ALU
Control
4
Instruction Reg
32
IRWr=1
Clk
PCWr=1
Clk
You are here!
One “Logic” Clock Cycle
取指结束时，新的PC值(PC+4)开始写入PC
即下个周期里，PC中已经是PC+4了。
取指结束时，当前指令开始写入IR ！为保证本指令期间IR中指令不变，后面周期中IRWr应该为0
Notes: As time goes by, the output of the memory will become valid and the ALU, with ALUOp sets to Add, will finish the 32-bit add.
Hopefully, we are smart enough to set the cycle time so the time between the clock tick is long enough to allow these (output of Memory and ALU) to stabilize.
So at the end of the cycle, the clock tick will trigger the Instruction Register to save the current instruction word (output of Instruction Memory).
Similarly, the Program Counter register is triggered (point to the clock input) to save the next instruction’s address (output of ALU).
Unlike the single cycle processor where a 30-bit PC can reduce the length of two adders by two bits, here we are using the 32-bit ALU to do the PC update anyway.
So the only saving we can get for using a 32 bit PC are two register bits. That’s why we didn’t bother to do it and keep a 32-bit Program Counter.
The Memory Unit here is also used to store data and the ALU here is also use for instruction execution. Therefore, we know we will need some MUXes in front of them.
+2 = 29 min. (Y:09)

## Slide 16: 考察整个取指周期（第一个周期）
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
IRWr=1
32
32
busA
32
busB
PCWr=1
ALUSelA=0
Mux
0
1
32
PC
Mux
0
1
32
0
1
2
3
4
ALUSelB=01
Mux
1
0
32
Zero
Zero
PCWrCond=x
PCSrc=0
BrWr=0
32
IorD=0
PC的更新时间
PC需要写使能信号（非每个周期都写）
多了一个指令寄存器IR
每个周期产生各自的控制信号
。。。。。。
想想看，和单周期有哪些不同？
1: PCWr, IRWr
ALUOp=Add
Others: 0s
x: PCWrCond
RegDst, Mem2R
Ifetch
分析：取指周期中各控制信号的取值应为？
Clk
分析的结果就是生成的一个“状态”，
在一个周期内发生作用
Notes: For example, the Memory can get its read address from the PC for instruction fetch but it can also get the read address from other part of the datapath for data fetch.
Similarly, the ALU can get its operands from the PC and a constant 4 as I showed you on the last slide, but we know the ALU can also gets its operands from the register file.
We will fill in the details here (Hole) later but for now, we know we need to set the control signals IorD, MemWr, ALUSelA, ALUSelB to zeros and IRWr and PCWr to 1s.
Notice that I have added a MUX in the PC feedback path because we know for the branch instruction, the next PC will have a value OTHER than PC plus 4 (ALU inputs).
We will worry about how we get this “other” value (Target) later. For this cycle, we have to set the MUX control (PCSrc) to zero to select the PC plus 4 value.
The settings of all the control signals are summarized in this circle. Due to space limitation, I have only shown the signals that have values other than zeros.
I want to emphasis that this is the picture at the END of the Instruction Fetch Cycle where evaluation is completed and control signals are settled.
This is the interesting part. The start of the cycle is boring by comparison. Consequently, all the datapath pictures I show from now on are the pictures at end of a cycle.
+2 = 31 min. (Y:11)

## Slide 17: 寄存器取 / 指令译码周期（第二个周期）
busA ← RegFile[rs] ; busB ← RegFile[rt] ;
Decoder ← Op and Func;
ALU 本周期内暂未使用: ALUctr = xx
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=xx
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=x
RegDst=x
Mux
0
1
32
PC
Mux
0
1
32
0
1
2
3
4
16
Imm
ALUSelB=xx
Mux
1
0
32
Zero
Zero
PCWrCond=0
PCSrc=x
32
IorD=x
Func
Op
Go to the
Control
6
6
指令未译码，故只执行公共操作
ALU空闲，可用ALU“投机计算”转移地址！
问题：PC中已是下条顺序指令的地址，对本条指令的执行有没有影响？
考虑转移地址投机计算的数据通路如何实现？
没有影响，因为IRWr=0!
Notes: Now that we have the instruction word saved in the IR, the next thing we can do is decode the instruction (Go to the Control) and fetch the registers from the Register file (Rs Rt).
I want to point out at this point, we do not know what instruction we have yet because we are still in the process of decoding the Op and Func field.
Therefore we are “jumping the gun” in fetching the registers Rs and Rt from the register file. The Rt field may not even be a source register if we have a I-type instruction.
But this is OK because if after we decode the instruction, we realize we don’t need the registers, we just don’t use them. No big deal.
Notice that the ALU is not being used in this cycle. That is not good. Instead of just letting the ALU sits idle, we may just as well let it do something.
***** Can we think of anyway we can use this ALU at this cycle? (see next slide)
We cannot use the ALU to do anything involving the registers because we are still in the process of reading them-we do not have the register values yet.
+2 = 33 min. (X:13)
Complement:
path from Rb to bus B is speculative because it might not be needed.

## Slide 18
busA ← Reg[rs] ; busB ← Reg[rt] ;
Decoder ← Op and Func;
投机：Target ← PC + SignExt(Imm16)*4
（为什么不是PC +4+ SignExt(Imm16)*4？）
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=0
RegDst=x
Mux
0
1
32
PC
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=10
Mux
1
0
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=1
32
IorD=x
Func
Op
Control
6
6
Beq
Rtype
Ori
Memory
:
为什么不直接送 PC? 为什么加BrWr?
寄存器取 / 指令译码周期（第二个周期）
指令译码
1: BrWr, ExtOp
ALUOp=Add
Others: 0s
x: RegDst, PCSrc
ALUSelB=10
IorD, MemtoReg
Rfetch/Decode
第二周期结束时，执行的结果是什么？
前两个周期的控制信号与指令无关
Notes: What we can do is to use this ALU to calculate the branch address in advance.
(1) We will set ALUSelA to 0 such that the PC is fed to the ALU input.
(2) The other ALU input will come from (ALUSelB=10) the Sign Extended (ExtOp=1)
version of the 16-bit immediate filed.
Once we added (ALUOp = Add) these two numbers together, we will save the result in the Target register (BrWr = 1). We cannot write the ALU output to the PC yet (PCWr = 0).
The OP and Func is still being decode in this cycle (Control) so we cannot update the PC to this value unless we are SURE we have a branch and the branch condition is met (AND-OR).
Once again, I have summarized all the control signals settings inside this circle. So far this and the Instruction Fetch cycles are shared by all instructions.
But by the end of this cycle, we will know exactly what instruction we have (Control output). Let’s say, we have a branch, what do we do?
+2 = 35 min. (Y:15)

## Slide 19: 寄存器取 / 指令译码周期（第二个周期）
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=0
RegDst=x
Mux
0
1
32
PC
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=10
Mux
1
0
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=1
32
IorD=x
Func
Op
Control
6
6
Ori
Memory
:
Rtype
Beq
如果指令译码输出为：Beq
下面第三个周期就是Beq指令的第一个执行周期！
Notes: Let’s go back to the end of the Register Fetch slash Instruction Decode Cycle.
Assume the result of the Instruction Decode indicates we have a R-type instruction, what do we do then? Well, simple enough: we just go to the R-type execution cycle.
+1 = 37 min. (Y:17)

## Slide 20: Branch指令执行并完成周期（第三个周期）
if (busA == busB)
  PC ← Target
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Sub
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
RegDst=x
Mux
0
1
32
PC
Extend
ExtOp=x
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=01
Mux
1
0
32
Zero
Zero
PCWrCond=1
PCSrc=1
BrWr=0
32
IorD=x
若不“投机”，则在此周期前还要加一个周期，用来计算转移地址后保存到Target中！
如果指令译码输出为：Branch
“ALU”每步都不空闲，被重复使用
1: PCWrCond
ALUOp=Sub
x: IorD, Mem2Reg
ALUSelB=01
RegDst, ExtOp
ALUSelA
BrFinish
PCSrc
PC是否在下个周期更新为Target，则由Zero决定！
控制信号的取值是什么？
Notes: We already have the values of registers Rs and Rt on busA and busB from last cycle, all we have to do is perform a Subtract (ALUOp) to compare them (ALUSelA, B).
If they are equal, the ALU’s Zero output will be asserted, and with PCSrc and PCWrCond set to one, the Branch Target will get written into the Program Counter. The Branch is taken.
If Rs and Rt are not equal, Zero will not be asserted and the Target value will NOT be written into the Program Counter. That is the Branch is NOT taken.
Since I am running out of space in this circle, I did not say it explicitly but all control signals not specified in this circle are default to zeros (point to the datapath for examples).
+1 = 36 min. (Y:16)

## Slide 21: 状态元件内容和控制信号取值的改变：在时钟到来后的一定延时后发生
周期1
取指令
(PC中为当前指令地址)
计算PC+4
周期2
译码
取寄存器
投机计算
PC+4 写入PC
指令 写入IR
控制信号：
PCwr=1
IRwr=1 …
控制信号：
PCwr=0
IRwr=0 …
信号和数据到达各处入口
投机计算结果到达target寄存器
周期3
Branch
减法
zero信号到达IFU
Target寄存器内容到达PC
虽然PCwr=0
但zero信号控制PC可写
另一条新指令的周期1
…
PC在时钟到来后的clock toＱ之后，完成写入。并保证在写入完成之前控制信号不会改变
如何保证？
看后面的控制器设计！
原来的PC+4被target替代
并送入mem开始取指
控制信号：
PCwr=1
IRwr=1 …
投机计算结果写入target寄存器
控制信号：
….

## Slide 22: 寄存器取 / 指令译码周期（第二个周期）
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=0
RegDst=x
Mux
0
1
32
PC
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=10
Mux
1
0
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=1
32
IorD=x
Func
Op
Control
6
6
Beq
Ori
Memory
:
Rtype
如果指令译码输出为：R-Type
第三个周期就是R-Type指令的第一个执行周期！
Notes: Let’s go back to the end of the Register Fetch slash Instruction Decode Cycle.
Assume the result of the Instruction Decode indicates we have a R-type instruction, what do we do then? Well, simple enough: we just go to the R-type execution cycle.
+1 = 37 min. (Y:17)

## Slide 23: R-type指令的执行周期（第三个周期，ALU运算）
ALU Output ← busA op busB
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Rtype
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=1
Mux
0
1
32
PC
MemtoReg=0
Extend
ExtOp=x
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=01
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=x
1: RegDst
ALUOp=Rtype
ALUSelB=01
x: PCSrc, IorD
MemtoReg
ALUSelA
ExtOp
RExec
为解决“Race”问题，该周期使RegDst=1，而使RegWr=0. Why?
R-type指令第一个周期控制信号取值？
保证地址Rw在写使能RegWr前先稳定，准备好下周期写
Notes: Once again, fetching the registers Rs and Rt in the previous cycle pays off. We need these two registers now and they are already on busA and busB, respectively.
So all we need is set the ALUSelA and ALUSelB to feed busA and busB into the ALU and tell the ALU local control we have a R-type instruction (ALUOp).
The ALU will then generate the correct result (ALU output) at the end of this cycle.
Notice that I have set RegDst to 1 here even though we are not writing the register file (RegWr is zero). Register file is not written until the next cycle.
You would think RegDst should be don’t care at this point.
****** Anybody want to guess why I set RegDst to 1 at this point?
Remember: for this Real memory and register file that do not have a clock input , the address (Rw) MUST be stable BEFORE we set Write Enable (RegWr) to one.
Here by setting RegDst to one, I can guarantee the Rw specifier will be stable by the next clock cycle where I will perform the write by setting RegWr to 1.
+2 = 39 min. (Y:19)

## Slide 24: R-type完成周期（第四个周期，写寄存器）
R[rd] ← ALU Output
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Rtype
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=1
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=1
Mux
0
1
32
PC
MemtoReg=0
Extend
ExtOp=x
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=01
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=x
R-type指令第二个周期控制信号取值？
RegDst=1 使Rw继续稳定
RegWr=1使busW的值写入
ALU输出必须保持稳定，直到本周期结束
1: RegDst, RegWr
ALUOp=Rtype
ALUselA
x: IorD, PCSrc
ALUSelB=01
ExtOp
Rfinish
Notes: So here is the picture where we finish off the R-type instruction by writing the ALU output back to the register file (MemtoReg=0 and RegWr = 1).
Notice that in order to keep the ALU output from changing, the ALUSelA, ALUSelB, and ALUOp control signals must remain the same as the previous cycle.
This brings us to a side topic I want to cover.
+1 = 40 min. (Y:20)

## Slide 25: 状态元件内容和控制信号取值的改变：在时钟到来后的一定延时后发生
周期1
取指令
(PC中为当前指令地址)
计算PC+4
周期2
译码
取寄存器
投机计算
PC+4 写入PC
指令 写入IR
控制信号：
PCwr=1
IRwr=1 …
控制信号：
PCwr=0
IRwr=0 …
信号和数据到达各处入口
投机计算结果到达target寄存器
周期3
R-type
ALU运算
运算结果到达寄存器组入口
另一条新指令的周期1
…
信息持续稳定在寄存器组入口，直到信号改变后将运算结果真正写入目标寄存器
投机计算结果写入target寄存器
控制信号：
Regwr=0
….
控制信号：
Regwr=1
….
周期4
在一定延迟后修改了控制信号
目标寄存器指定

## Slide 26
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Intruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=0
RegDst=x
Mux
0
1
32
PC
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=10
Mux
1
0
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=1
32
IorD=x
Func
Op
Control
6
6
Beq
Rtype
Memory
:
寄存器取 / 指令译码周期（第二个周期）
Ori
指令译码输出为：ori
下面第三个周期就是ori指令的第一个执行周期！
Notes: Let’s go back to the end of the Register Fetch slash Instruction Decode Cycle.
Assume the result of the Instruction Decode indicates we have a OR immediate instruction, what do we do then? Well, we go to the OR immediate execution cycle.
+1 = 56 min. (Y:36)

## Slide 27: Ori 指令执行周期（第三个周期，ALU运算）
ALU output ← busA or ZeroExt[Imm16]
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Or
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=0
Mux
0
1
32
PC
MemtoReg=0
Extend
ExtOp=0
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=11
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=x
为解决“Race”问题，该周期使RegDst=0，而使RegWr=0
ori指令的第一个周期，控制信号取值？
ALUOp=Or
IorD, PCSrc
1: ALUSelA
ALUSelB=11
x: MemtoReg
OriExec
Notes: The first operand of OR immediate comes from register Rs. It is already on busA so we just set ALUSelA to 1.
The second operand, on the other hand, does NOT come from Rt. It comes from the Zero Extended (ExtOp = 0) version of the immediate field (ALUSelB = 11).
Once we have the operands, all we have to do is to ask the ALU to OR (ALUop) them together and the ALU output will have the correct result at the end of this cycle.
Notice that I have set RegDst to zero so the Rt field of the instruction word will be stable at Register File’s Rw address port before the next cycle.
What do we do in the next cycle?
+2 = 58 min. (Y:38)

## Slide 28: Ori 指令完成周期（第四个周期，写寄存器）
R [rt] ← ALU output
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Or
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=1
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=0
Mux
0
1
32
PC
MemtoReg=0
Extend
ExtOp=0
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=11
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=x
RegDst=0使Rw继续稳定，RegWr=1使busW上的值写入 （流程同本课件101页的图）
ori指令的第二个周期控制信号取值？
1: ALUSelA
ALUOp=Or
x: IorD, PCSrc
RegWr
ALUSelB=11
OriFinish
Notes: Well we do a register write (RegWr=1).
Once again, I have set up the register write address Rw in advance (RegDst = 0) during the previous cycle so I can guarantee Rw is stable when I assert RegWr in this cycle.
Also, remember we have a multiple cycle delay path from the Instruction Register to the Register File Write Port.
Therefore, IRWr must be 0 and ALUSelA & B, and ALUOp must remain the same as the previous cycle in order to guarantee ALU output to be stable during register write.
+1 = 59 min. (Y:39)

## Slide 29
Target
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=0
RegDst=x
Mux
0
1
32
PC
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=10
Mux
1
0
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=1
32
IorD=x
Func
Op
Control
6
6
Beq
Rtype
Ori
:
寄存器取 / 指令译码周期（第二个周期）
Mem
指令译码输出：访存指令（lw 或 sw）
第三个周期就是lw/sw指令的第一个周期！
Notes: Let’s go back to the end of the Register Fetch slash Instruction Decode Cycle.
Assume the result of the Instruction Decode indicates we have a memory access instruction, that is we either have a load or store.
The next cycle we need to get into is the Memory Address Calculation cycle.
+1 = 60 min. (Y:40)

## Slide 30: lw/sw内存地址计算周期（第三个周期，ALU运算）
ALUOp=Add
PCSrc
1: ExtOp
ALUSelB=11
x: MemtoReg
ALUSelA
MemAdr
ALU output ← busA + SignExt[Imm16]
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=x
Mux
0
1
32
PC
MemtoReg=x
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=11
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=1
lw/sw指令的第一个周期控制信号取值？
ALU的输出可能是读地址，也可能是写地址！
Notes: How do we calculate the memory address?
Simple, we have to add the contents of register Rs (busA) to the Sign Extended (ExtOp=1) version of the Immediate field (ALUSelB = 11).
With the ALUOp set to add, the memory address will be valid at the ALU output by the end of this cycle.
Let’s say we do have a store instruction and see what happens next.
+1 = 61 min. (Y:41)

## Slide 31: sw指令存数周期（第四周期，访存写）
M[ALU output] ← busB
Real
Memory
Din
Adr
32
32
Dout
MemWr=1
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=x
Mux
0
1
32
PC
MemtoReg=x
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=11
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=1
ALUOp=Add
x: PCSrc,RegDst
1: ExtOp
ALUSelB=11
MemtoReg
MemWr
ALUSelA
swFinish
sw指令的第二个周期，控制信号取值？
必须保持 ALUSelA, ALUSelB, ALUOp与上个周期取值相同! 以保证Adr稳定不变！
Notes: Well, the address is already set up at the Memory’s write address port.
The data is also already available on the Memory’s data port via busB.
Therefore, all we have to do is to set MemWr to 1.
Notice that it is very important that we keep ALUSelA, ALUSelB, and ALUOp the same as the previous cycle, the Memory Address calculation cycle.
Otherwise, if any of these control signals changes during Memory Write, the address will also change because we do not have a register to save the ALU output.
Any changes in the address during this cycle with MemWr = 1 will have catastrophic result. We will end up destroying data stored in memory by writing to the wrong address location.
+2 = 63 min. (Y:43)

## Slide 32: lw指令取数周期（第四周期，访存读）
Mem Dout ← M[ALU output]
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=0
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=0
Mux
0
1
32
PC
MemtoReg=1
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=11
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=1
lw指令的第二个周期，控制信号取值？
RegDst=0,RegWr=0,MemtoReg=1使Rw和busW在RegWr=1前先稳定
ALUOp=Add
x: MemtoReg
1: ExtOp
ALUSelB=11
ALUSelA, IorD
PCSrc
MemFetch
Notes: If after the Memory Address calculation cycle, we realize we have a load.
We then enter the Load Memory Access cycle.
All we have to do is set the control signal IorD to 1 then after the memory read access delay, the data we want will be available at the output of the Ideal Memory (Dout).
Once again, we need to set RegDst to zero in this cycle so Rt will be stabilized at the Register file’s write address port (Rw) before next cycle.
+2 = 45 min. (Y:45)

## Slide 33: lw指令回写周期（第五周期，写寄存器）
R[rt] ← Mem Dout
Real
Memory
Din
Adr
32
32
Dout
MemWr=0
32
ALU
32
32
ALUOp=Add
ALU
Control
Instruction Reg
32
IRWr=0
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr=1
Rs
Rt
Mux
0
1
Rt
Rd
PCWr=0
ALUSelA=1
Mux
0
1
RegDst=0
Mux
0
1
32
PC
MemtoReg=1
Extend
ExtOp=1
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB=11
Mux
1
0
Target
32
Zero
Zero
PCWrCond=0
PCSrc=x
BrWr=0
32
IorD=1
ALUOp=Add
x: PCSrc
1: ALUSelA
ALUSelB=11
MemtoReg
RegWr, ExtOp
lwFinish
lw指令的第三个周期，控制信号取值？
RegDst=0,RegWr=1使Rw在RegWr=1后继续保持稳定
ALU输出在ALU控制不变时保持稳定，以使Dout和busW保持稳定。
Notes: Because in this next cycle, the Write Back cycle, we will write the data from memory (MemtoReg = 1) into the register specified by the Rt field of the instruction.
+1 = 66 min. (Y:46)

## Slide 34: 状态元件内容和控制信号取值的改变：在时钟到来后的一定延时后发生
周期1
取指令
(PC中为当前指令地址)
计算PC+4
周期2
译码
取寄存器
投机计算
PC+4 写入PC
指令 写入IR
控制信号：
PCwr=1
IRwr=1 …
控制信号：
PCwr=0
IRwr=0 …
信号和数据到达各处入口
投机计算结果到达target寄存器
周期3
Lw/sw
ALU运算
运算结果(地址)到达Mem入口
另一条新指令的周期1
…
投机计算结果写入target寄存器
控制信号：
Memwr=0
….
控制信号：
Memwr=1
….
周期4
Sw
在一定延迟后修改了控制信号
寄存器读出数据到达mem入口
信息持续稳定在mem入口，直到信号改变后将数据真正写入mem

## Slide 35: 状态元件内容和控制信号取值的改变：在时钟到来后的一定延时后发生
周期1
取指令
(PC中为当前指令地址)
计算PC+4
周期2
译码
取寄存器
投机计算
PC+4 写入PC
指令 写入IR
控制信号：
PCwr=1
IRwr=1 …
控制信号：
PCwr=0
IRwr=0 …
信号和数据到达各处入口
投机计算结果到达target寄存器
周期3
Lw/sw
ALU运算
运算结果(地址)到达Mem入口
另一条新指令的周期1
…
投机计算结果写入target寄存器
控制信号：
Memwr=0
….
控制信号：
Memwr=0
Regwr=0
….
周期4
Lw
Mem读出数据送到寄存器组入口
目标寄存器指定
控制信号：
Memwr=0
Regwr=1
….
周期5
在一定延迟后修改了控制信号
信息持续稳定在寄存器组入口，直到信号改变后将load结果真正写入目标寄存器

## Slide 36: 完成前述指令的完整多周期数据通路（没有Jump）
Ideal
Memory
Din
Adr
32
32
Dout
MemWr
32
ALU
32
32
ALUOp
ALU
Control
Instruction Reg
32
IRWr
32
Reg File
Ra
Rw
busW
Rb
5
5
32
busA
32
busB
RegWr
Rs
Rt
Mux
0
1
Rt
Rd
PCWr
ALUSelA
Mux
0
1
RegDst
Mux
0
1
32
PC
MemtoReg
Extend
ExtOp
Mux
0
1
32
0
1
2
3
4
16
Imm
32
<< 2
ALUSelB
Mux
1
0
Target
32
Zero
Zero
PCWrCond
PCSrc
BrWr
32
IorD
和书中的图有一些不同
下面关键是如何控制在不同周期产生不同的控制信号取值！这就是控制器的任务。下面考虑如何设计控制器！
Notes: Putting it all together, here it is: the multiple cycle datapath we set out to built.
+1 = 47 min. (Y:47)

## Slide 37: 状态转换图
下一步目标：设计“状态转换电路” 即：控制器
问题：各指令的时钟数多少？
每来一个时钟，进入下一个状态
R-4, ori-4, beq-3, Jump-3, lw-5, sw-4
每个状态下，输出的控制信号有相应的不同取值！
BACK
Notes: Well, we pretty much concentrated on the multiple cycle datapath today.
But if you think about it, by summarizing all the control signals in circles along the way, we have pretty much specified the control in a state diagram.
All instructions start out at the Instruction Fetch cycle and continue to the Instruction Decode slash Register Fetch cycle.
Once the instruction is decoded, we will either go to the Branch Complete cycle to complete the branch or go to one of the following:
(1) R-type executioin or OR immediate execution for R-type or Or immediate instructions.
(2) Or we will go to the memory address calculation cycle for load and store instrution.
The rest is pretty straight forward.
+5 = 75 min. (Y:55)

## Slide 38: 多周期控制器的实现
多周期控制器功能描述方式：
有限状态机：
  采用组合逻辑设计
  用硬连线路(PLA)实现
微程序：
  用ROM存放微程序实现
回忆单周期控制器的实现：控制信号在整个指令执行过程中不变，用真值表能反映指令和控制信号的关系。根据真值表就能实现控制器！
多周期控制器能不能这样做？
不可以，因为：
每个指令有多个周期，每个周期控制信号取值不同！

## Slide 39: 多周期控制器的实现

## Slide 43: 小结
单周期CPU和多周期CPU的成本比较：
  单周期下功能部件不能重复使用；而多周期下可重复使用，比单周期省
  单周期指令执行结果直接保存在PC、Regfile和Memory；而多周期下需加一些临时寄存器保存中间结果，比单周期费
单周期CPU和多周期CPU的性能比较：
  单周期CPU的CPI为1，但时钟周期为最长的load指令执行时间
  多周期CPU的CPI是多少？时钟周期多长？
  假定程序中22%为Load，11%为Store，49%为R-Type，16%为Branch，2%为Jump。每个状态需要一个时钟周期，CPI为多少？
  分析如下：每种指令所需的时钟周期数为：
  Load：5；Store：4；R-Type：4；Branch：3；Jump：3
  CPI=CPU时钟周期数 / 指令数 = Σ（指令数 i x CPI i ）/ 指令数
  = Σ（指令数 i / 指令数 ）x CPI i
  CPI = 0.22x5+0.11x4+0.49x4+0.16x3+0.02x3 = 4.04
  假设单周期时钟宽度为1，则多周期时钟周期约为单周期的1/5，所以，
  多周期的总体时间约：4.04x1/5=0.8（其实不可能，也许只是1/3，那么4.04x1/3 > 1）；而单周期总体时间为：1x1=1
  由此看出：划分阶段很均匀时，多周期可能比单周期效率高！